## Slide 1
OCR GCSE COMBINED SCIENCE B (TWENTY FIRST CENTURY)
C4.1 Choosing materials
How is data used to choose a material for a particular use?
Metals • Ceramics • Polymers • Composites • Alloys • Density
§
Specification C4.1.1–C4.1.3 • metals, ceramics, polymers, composites, alloys
H
Higher & Foundation in one deck • no Higher-only statement found • stretch marked
▲
Data: density, strength, melting point • density practical • alloy composition
Part 1 of 4 in Chapter C4: Material choices
OCR J260 Combined Science B • C4.1 How is data used to choose a material for a particular use? • teacher deck • mark schemes in the notes
Notes: C4.1 How is data used to choose a material for a particular use? is Part 1 of 4 in J260 Chapter C4 Material choices. J260 C4 sub-topics (see SPEC_C4_1.md): C4.1 choosing materials with data; C4.2 How do bonding and structure affect properties of materials?; C4.3 Why are nanoparticles so useful?; C4.4 What happens to products at the end of their useful life? (life-cycle assessment). J258 (Chemistry B) has an extra C4.2 "What are the different types of polymers?" which is separate science only, so J258 C4.3–C4.5 become J260 C4.2–C4.4. Statements C4.1.1–C4.1.3 are from search extracts of the J258 wording (C4.1 is common to both specifications). C4.1.3 (alloys) has medium confidence for J260. No HT marker was found for C4.1.

## Slide 2
Learning objectives
Specification C4.1.1–C4.1.3 • by the end of this sub-topic you can…
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Objectives | 2
1
C4.1.1 Name the four families: metals, ceramics (glass and clay), polymers and composites.
2
C4.1.1 Describe properties: strength (tension, compression), stiffness, flexibility, brittleness, hardness.
3
C4.1.1 Compare materials quantitatively using data: density, melting / softening point, strength, conductivity.
4
C4.1.1 Describe glass and clay ceramics, polymers and composites and their typical properties.
5
C4.1.2 Explain how properties relate to uses and select a material from a specification and data.
6
C4.1.3 Describe the composition of important alloys, including steel, linked to properties and uses.
7
C4.1.1 Measure density by displacement; plot mass against volume and use the gradient.
8
C4.1.2 Evaluate a material choice by weighing benefits against cost and other drawbacks.
Notes: Statements (J258 C4.1 wording from search extracts; C4.1 is in both J258 and J260): C4.1.1 compare quantitatively the physical properties of glass and clay ceramics, polymers, composites and metals (to include melting point, softening temperature for polymers, electrical conductivity, strength in tension or compression, stiffness, flexibility, brittleness, hardness, density, ease of reshaping) C4.1.2 explain how the properties of materials are related to their uses and select appropriate materials given details of the usage required C4.1.3 describe the composition of some important alloys in relation to their properties and uses (including steel) No Higher-only (bold) statement was found for C4.1. Strength per unit density is marked GRADE 7–9 STRETCH. Maths: density, ratios, percentages, means, reading and plotting graphs, gradient. The density practical is a suggested practical (no PAG link found).

## Slide 3
Where this fits
Chapter C4 Material choices • C4.1 is Part 1 of 4 in Combined Science B
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Context | 3
C4.1
Choosing materials
C4.1.1 Four families of materials; describing properties
BOTH TIERS
C4.1.1 Comparing materials with data: ceramics, polymers, composites
BOTH TIERS
C4.1.2 Choosing a material from a specification
BOTH TIERS
C4.1.3 Alloys: steel, stainless steel, brass, gold
BOTH TIERS
Practical Measuring density by displacement
PRACTICAL
C4.1.2 Evaluating a choice: car body panels
BOTH TIERS
Earlier links: C1 particle model • C2 metals and non-metals, ionic compounds • C3 metals and extraction
Chapter C4 in J260
C4.1 How is data used to choose a material for a particular use? (this deck)
C4.2 How do bonding and structure affect properties of materials?
C4.3 Why are nanoparticles so useful?
C4.4 What happens to products at the end of their useful life?
One deck for both tiers
No Higher-only statement was found for C4.1. Strength per unit density is marked GRADE 7–9 STRETCH.
This deck asks what the properties are; C4.2 explains why, using bonding and structure.
Maths: density = mass ÷ volume, ratios, percentages, plotting a graph and finding a gradient.
Notes: J260 Chapter C4 Material choices has four sub-topics (SPEC_C4_1.md): C4.1 data and choosing materials; C4.2 bonding and structure (J258 C4.3); C4.3 nanoparticles (J258 C4.4); C4.4 life cycle of materials / LCA (J258 C4.5). J258 C4.2 on polymer types (addition, condensation, natural polymers) is separate science only. Overlap control: this deck describes properties and uses with data. WHY metals conduct, why polymers soften and why alloys are harder are explained with bonding and structure in C4.2; here they are previewed with simple particle pictures only. Nanoparticles are C4.3. Recycling, landfill and life-cycle assessment are C4.4 and are mentioned only (slide 18). Recall links (UNVERIFIED sub-codes): C1 particle model and states; C2 periodic table, metals vs non-metals, ionic compounds; C3 metallic bonding and extraction of metals.

## Slide 4
Retrieval starter
Recall from C1, C2, C3 and KS3 • 6 minutes • no notes
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Starter | 4
1
C3 • metals
Describe the structure of a metal. Why can metals conduct electricity?
2
C3 • extraction
Balance: Fe₂O₃(s) + __CO(g) → __Fe(l) + __CO₂(g). What is reduced?
3
C2 • periodic table
Give three physical properties of metals that most non-metals do not have.
4
C1 • particle model
What happens to the particles when a solid melts? Why do substances melt at different temperatures?
5
C2 • ionic compounds
Why does sodium chloride have a high melting point? Why does the solid not conduct?
6
KS3 • maths
A block has mass 54 g and volume 20 cm³. Calculate its density and give the unit.
Self-mark Swap and mark from the answers. 6/6 secure • 4–5 nearly there • 0–3 revisit the topic notes
Notes: ANSWERS 1. A giant regular lattice of positive metal ions in a "sea" of delocalised electrons. The delocalised electrons are free to move through the structure, carrying charge. 2. Fe₂O₃(s) + 3CO(g) → 2Fe(l) + 3CO₂(g). Iron(III) oxide is reduced (loses oxygen); carbon monoxide is oxidised. 3. Any three: shiny; conduct electricity; conduct heat; malleable / ductile; high density; high melting point (most); sonorous. 4. Particles gain energy, vibrate more, overcome some of the forces of attraction and can move past each other. Different substances have different strengths of forces / bonds between particles. 5. Giant ionic lattice with strong electrostatic attraction between oppositely charged ions in all directions: lots of energy is needed to overcome them. In the solid the ions are fixed in place and cannot move. 6. 54 ÷ 20 = 2.7 g/cm³ (aluminium). Chapter codes for recall are UNVERIFIED (J260 C1 Air and water, C2 Chemical patterns, C3 Chemicals of the natural environment).

## Slide 5
Four families of materials
Specification C4.1.1 • metals, ceramics, polymers and composites
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
C4.1.1 | 5
Illustrative diagram — particle and structure pictures, simplified; not to scale
Metals
Ceramics
Polymers
Composites
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
ions in layers + free electrons
glass
fired clay
long chain molecules
fibres set in a matrix
Examples: steel, copper • glass, brick, pottery • poly(ethene), PVC • carbon fibre, concrete
The four families
Metals (and alloys): strong, tough, shiny, good conductors of heat and electricity, can be bent or hammered into shape.
Ceramics: glass and clay ceramics (brick, pottery). Hard, stiff, high melting point, but brittle; electrical insulators.
Polymers (plastics, rubber): low density, flexible, insulators, soften at low temperatures, easy to mould.
Composites: two or more materials combined, e.g. fibres in a resin, to get properties neither has alone.
Worked example: identify a metal
A sample has mass 39 g and volume 5.0 cm³.
1 Equation density = mass ÷ volume
2 Substitute 39 ÷ 5.0 = 7.8 g/cm³
3 Answer matches steel (7.8 g/cm³) in the data table
Quick check Name the family for: brick, carbon-fibre bike, PVC pipe, copper wire. A 13.5 g sample has a volume of 5.0 cm³: density?
Notes: QUICK CHECK ANSWER: brick = ceramic (clay); carbon-fibre bike = composite; PVC pipe = polymer; copper wire = metal. 13.5 ÷ 5.0 = 2.7 g/cm³ (aluminium). C4.1.1 names glass and clay ceramics, polymers, composites and metals. The particle pictures are a preview only: C4.2 explains properties with bonding and structure (metallic lattice, giant covalent networks, polymer chains). Density alone does not prove identity: other materials can share a density (IaS: use more than one property).

## Slide 6
Describing properties
Specification C4.1.1 • the words scientists and engineers use
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
C4.1.1 | 6
Illustrative diagram — how each property is tested; forces shown as arrows; not to scale
Strength in tension
Strength in compression
Stiff or flexible?
Hard or brittle?
pulled: does it snap?
e.g. rope, cable, bridge wire
squashed: does it crush? e.g. pillar, brick
stiff
flexible
same load: how far does it bend?
scratch test
snaps with no bending: brittle
opposite of brittle: tough
Property words
Strength: the force needed to break it. Tension = pulling; compression = squashing.
Stiffness: how hard it is to bend or stretch. Opposite: flexible.
Hardness: how hard it is to scratch or dent. Brittle: breaks suddenly without bending.
Density: mass per unit volume (g/cm³). Melting point; polymers have a softening temperature.
Electrical conductivity; ease of reshaping (can it be bent, rolled or moulded?).
Worked example: tension or compression?
Concrete: strength in compression 30 MPa; in tension 3 MPa.
1 Ratio 30 ÷ 3 = 10
2 Answer 10 times stronger when squashed than when pulled
Quick check What is the difference between hard and tough? Glass: compression 1000 MPa, tension 50 MPa. How many times stronger in compression?
Notes: QUICK CHECK ANSWER: Hard = resists scratching / denting; tough = absorbs energy and does not break easily (bends before breaking; opposite of brittle). A material can be hard but brittle (glass). 1000 ÷ 50 = 20 times. 1 MPa = 1 N/mm² (megapascal). Values for glass and concrete are typical, rounded (illustrative). These are the C4.1.1 property words: melting point, softening temperature for polymers, electrical conductivity, strength in tension or compression, stiffness, flexibility, brittleness, hardness, density, ease of reshaping.

## Slide 7
Exam practice: recap 1
Specification C4.1.1 • families and properties
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Recap 1 | 7
EXAM-STYLE QUESTION
Name the four families of materials and give one example of each.
[2 marks]
EXAM-STYLE QUESTION
Explain what is meant by a brittle material. Give one example.
[2 marks]
EXAM-STYLE QUESTION
A sample has mass 31.2 g and volume 4.0 cm³. Calculate its density.
[2 marks]
EXAM-STYLE QUESTION
Explain why concrete beams are reinforced with steel bars along the bottom, where they are stretched.
[2 marks]
Notes: MARK SCHEME — Recap 1 (total 8 marks) Q1 [2]: All four families named (1): metals, ceramics, polymers, composites; one correct example for each (1), e.g. steel, glass / brick, poly(ethene), carbon fibre / concrete. Q2 [2]: Breaks / shatters suddenly without bending / changing shape first (1); glass / pottery / brick / ceramic (1). Q3 [2]: 31.2 ÷ 4.0 (1); = 7.8 g/cm³ (1). Unit needed for the second mark. Q4 [2]: Concrete is weak in tension / strong only in compression (1); steel is strong in tension, so the bars stop the beam cracking where it is pulled (1).

## Slide 8
Comparing materials with data
Specification C4.1.1 • quantitative comparison of the four families
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
C4.1.1 | 8
Illustrative diagram — bar chart drawn to scale from the table (typical values, rounded)
Density / g/cm³
Steel
Al alloy
Copper
Glass
Brick
HDPE
GRP
CFRP
7.8
2.7
8.9
2.5
1.9
0.95
1.9
1.6
metal
ceramic
polymer
composite
Metals are the densest; polymers and composites are light. Ceramics are in between.
Material | Density g/cm³ | Melts / softens °C | Tensile strength MPa | Conducts?
Steel (mild) | 7.8 | 1450 | 400 | good
Aluminium alloy | 2.7 | 640 | 300 | good
Copper | 8.9 | 1085 | 220 | very good
Soda-lime glass | 2.5 | 720 | 50 | no
Clay brick | 1.9 | 1600 | 5 | no
Poly(ethene) HDPE | 0.95 | 130 | 30 | no
Glass-fibre (GRP) | 1.9 | 200 | 250 | no
Carbon-fibre (CFRP) | 1.6 | 200 | 1000 | slight
Worked example: replacing steel with aluminium
A steel bracket has mass 2.0 kg. A bracket of the same size is made from aluminium alloy.
1 Ratio 7.8 ÷ 2.7 = 2.9 (steel is 2.9 × denser)
2 Mass 2.0 × 2.7 ÷ 7.8 = 0.692 kg
3 Answer about 0.69 kg, but alloy is weaker, so it may need to be thicker
Quick check Which material in the table has the lowest softening temperature? How many times denser is copper than HDPE?
Notes: QUICK CHECK ANSWER: HDPE poly(ethene), about 130 °C. 8.9 ÷ 0.95 = 9.4 times (2 s.f.). All values are typical, rounded textbook values (UNVERIFIED to the exact figure; real values depend on grade). Glass softens over a range (soda-lime about 700–730 °C) rather than melting sharply; polymers soften. Clay brick: fired clay does not melt below about 1500 °C. CFRP conducts slightly because carbon fibres conduct. Node: 2.0 × 2.7 ÷ 7.8 = 0.6923 kg; bracket volume 2000 g ÷ 7.8 = 256 cm³.

## Slide 9
Ceramics: glass and clay
Specification C4.1.1 • properties and uses of glass and clay ceramics
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
C4.1.1 | 9
Illustrative diagram — glass: disordered network; fired clay: crystals bonded together
Glass
silicon
oxygen
Fired clay (brick, pottery)
heated in a kiln to about 1000 °C
Making glass: heat sand (SiO₂) with sodium carbonate and limestone to about 1500 °C
Na₂CO₃(s) + SiO₂(s) → Na₂SiO₃(l) + CO₂(g)
Clay is soft and easy to shape when wet; firing makes it hard and rigid
Borosilicate glass (oven dishes, test tubes) softens at a higher temperature than soda-lime glass
Properties → uses
Both: hard, stiff, brittle, high melting point, strong in compression but weak in tension, electrical and heat insulators, do not corrode.
Glass: transparent → windows, bottles, lenses, optical fibres; can be melted and reshaped when hot.
Clay ceramics: cheap, hard, resist heat and water → bricks, tiles, plates, sinks, toilets, insulators on pylons.
Their main weakness: they shatter when hit or bent.
Worked example: density of a brick
A brick is 21.5 cm × 10.25 cm × 6.5 cm and has a mass of 2.7 kg.
1 Volume 21.5 × 10.25 × 6.5 = 1432 cm³
2 Density 2700 g ÷ 1432 cm³ = 1.885
3 Answer 1.9 g/cm³ (2 s.f.)
Quick check Give two properties of glass that make it suitable for windows. A tile has mass 20 g and volume 8.0 cm³: density?
Notes: QUICK CHECK ANSWER: Transparent; hard (scratch-resistant); does not corrode / is waterproof; electrical insulator not relevant. 20 ÷ 8.0 = 2.5 g/cm³. Glass equation (atom balance asserted in node): Na₂CO₃(s) + SiO₂(s) → Na₂SiO₃(l) + CO₂(g). Limestone first decomposes: CaCO₃(s) → CaO(s) + CO₂(g); CaO makes the glass insoluble. These equations are context, not a recall requirement (UNVERIFIED that J260 requires them). Glass is amorphous (no regular lattice): C4.2 deals with structure. Node: brick volume 1432.4375 cm³, density 1.885 g/cm³.

## Slide 10
Polymers and composites
Specification C4.1.1 • light, mouldable polymers and materials combined for strength
GRADE 7–9 STRETCH
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
C4.1.1 | 10
Illustrative diagram — polymer chains; fibres in a resin matrix; reinforced concrete
Polymer: long chains
heat → chains slide → softens
Composite: fibres + matrix
fibres: strong in tension • resin: binds
Reinforced concrete: steel bars set in concrete (a composite)
load
concrete takes the compression (top) • steel takes the tension (bottom)
Other composites: GRP (boats), CFRP (bikes, racing cars), plywood, MDF
Properties → uses
Polymers: low density, flexible or tough, insulators, waterproof, low softening temperature, easy to mould → bags, bottles, pipes, cable insulation.
Composites combine materials: CFRP and GRP are strong, stiff and very light → bike frames, boats, aircraft parts; but expensive and hard to recycle.
Reinforced concrete: strong in compression and tension → beams, bridges.
Stretch: strength per unit density
Tensile strength ÷ density (MPa per g/cm³), from the data table.
1 Steel 400 ÷ 7.8 = 51
2 CFRP 1000 ÷ 1.6 = 625
3 Answer CFRP is about 12 times stronger for its mass
Quick check Why are electrical cables coated in a polymer? Calculate strength ÷ density for GRP (250 MPa, 1.9 g/cm³).
Notes: QUICK CHECK ANSWER: Polymers are electrical insulators (and flexible, waterproof), so the cable is safe to touch and can bend. 250 ÷ 1.9 = 132 (3 s.f.). GRADE 7–9 STRETCH: "strength per unit density" (specific strength) is not a named J260 term; it is a useful way to compare data for lightweight uses. Node: steel 51.3, aluminium 111, CFRP 625, ratio CFRP/steel 12.2. Polymer types (addition / condensation, natural polymers) are J258 C4.2, separate science only: not taught here. Why polymers soften (weak forces between chains) is C4.2.

## Slide 11
Exam practice: recap 2
Specification C4.1.1 • using data on materials
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Recap 2 | 11
EXAM-STYLE QUESTION
Use the data table: give two properties of poly(ethene) that make it better than glass for a drinks bottle.
[2 marks]
EXAM-STYLE QUESTION
Copper has density 8.9 g/cm³ and aluminium 2.7 g/cm³. How many times denser is copper? (2 s.f.)
[2 marks]
EXAM-STYLE QUESTION
Explain why glass is used for windows but not for car bumpers.
[2 marks]
EXAM-STYLE QUESTION
Explain what a composite material is, using GRP as an example.
[2 marks]
Notes: MARK SCHEME — Recap 2 (total 8 marks) Q1 [2]: Any two (1 each): lower density / lighter; not brittle / does not shatter / tough / flexible; easy to mould. Q2 [2]: 8.9 ÷ 2.7 (1); = 3.3 (1). Q3 [2]: Glass is transparent / hard / does not corrode, so suits windows (1); glass is brittle / shatters on impact, so unsuitable for bumpers (1). Q4 [2]: Made of two or more materials combined / fibres in a matrix (1); GRP = glass fibres in a polymer resin, giving strong light material (1).

## Slide 12
Choosing a material for a use
Specification C4.1.2 • from a specification to a decision
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
C4.1.2 | 12
Illustrative diagram — design steps and a bike frame; frame masses calculated for 400 cm³ of material
1 Write the specification: what must it do?
2 List the properties needed
3 Shortlist materials using data
4 Weigh up cost, safety, appearance
5 Decide and justify
Bike frame: strong, stiff, light, does not rust
Frame | Density | Mass | Cost
Steel | 7.8 | 3.12 kg | low
Aluminium alloy | 2.7 | 1.08 kg | medium
CFRP | 1.6 | 0.64 kg | high
Racing bike → CFRP (light). Cheap, tough commuter bike → steel.
Properties decide the use
Saucepan: metal body (conducts heat, high melting point); polymer handle (heat insulator).
Electric cable: copper core (best conductor, ductile); PVC coat (insulator, flexible).
Aircraft: aluminium alloys and CFRP (strong but low density).
Bridge: steel and reinforced concrete (strong in tension and compression, cheap in bulk).
There is rarely a perfect material: choose the best compromise.
Worked example: frame mass from density
400 cm³ of material is used to make the frame.
1 Equation mass = density × volume
2 Steel 7.8 × 400 = 3120 g; CFRP: 1.6 × 400 = 640 g
3 Answer CFRP saves 3120 − 640 = 2480 g = 2.48 kg
Quick check Explain why a saucepan handle is made of a polymer. Calculate the % mass saved by using aluminium instead of steel (2 s.f.).
Notes: QUICK CHECK ANSWER: Polymer is a poor conductor of heat (insulator) so the handle stays cool; also light and mouldable (a thermosetting polymer does not soften when hot). (3120 − 1080) ÷ 3120 × 100 = 65% (2 s.f.). C4.1.2: explain how the properties of materials are related to their uses and select appropriate materials given details of the usage required. Using the same volume for each frame is a simplification (illustrative): real frames use different tube thicknesses because the materials have different strengths and stiffness. Costs are qualitative.

## Slide 13
Alloys: steel and others
Specification C4.1.3 • composition linked to properties and uses
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
C4.1.3 | 13
Illustrative diagram — atoms as circles in layers; bar drawn to scale (by mass)
Pure iron: regular layers
layers slide easily: soft
Alloy: other atoms added
layers distorted: harder, stronger
carbon atom
larger atom
Stainless steel composition by mass
Iron 74%
Chromium 18%
Nickel 8%
Making steel: blow oxygen through molten iron to burn off extra carbon
C(s) + O₂(g) → CO₂(g)
then add exact amounts of carbon and other metals
Alloy | Composition (typical) | Property → use
Mild steel | iron + about 0.25% carbon | strong, easily shaped → car bodies, girders
High-carbon steel | iron + about 1% carbon | very hard, more brittle → tools, blades
Stainless steel | iron + 18% chromium + 8% nickel | does not rust → cutlery, sinks
Brass | 70% copper + 30% zinc | harder than copper, gold colour → taps, plug pins
Bronze | about 88% copper + 12% tin | hard, resists corrosion → statues, bells
18-carat gold | 75% gold + silver / copper | harder than pure gold → jewellery
Worked example: mass of a metal in an alloy
A stainless steel sink has a mass of 2.0 kg. It is 18% chromium.
1 Fraction 18% = 0.18
2 Answer 2.0 × 0.18 = 0.36 kg of chromium
Quick check Why is stainless steel used for cutlery rather than mild steel? What percentage of 9-carat gold is gold? (carat = parts in 24)
Notes: QUICK CHECK ANSWER: Stainless steel does not rust / corrode (chromium forms a protective oxide layer); mild steel rusts: 4Fe(s) + 3O₂(g) + 6H₂O(l) → 4Fe(OH)₃(s). 9 ÷ 24 × 100 = 37.5%. C4.1.3 (J258 wording, search extract): describe the composition of some important alloys in relation to their properties and uses, including steel. Confidence that it is in J260: medium. Compositions are typical (UNVERIFIED exact percentages; stainless 18/8 is the common grade 304). Why alloys are harder (distorted layers) is previewed here and explained with metallic bonding in C4.2. Node: 18/24 = 75%; 0.25% of 500 kg = 1.25 kg carbon; 70% of 200 g brass = 140 g copper.

## Slide 14
Exam practice: recap 3
Specification C4.1.2, C4.1.3 • choosing materials and alloys
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Recap 3 | 14
EXAM-STYLE QUESTION
Explain why copper is used for the core of an electrical cable and PVC for the outside.
[2 marks]
EXAM-STYLE QUESTION
What is an alloy? Give one reason why alloys are often more useful than pure metals.
[2 marks]
EXAM-STYLE QUESTION
A stainless steel spoon of mass 250 g contains 18% chromium. Calculate the mass of chromium.
[2 marks]
EXAM-STYLE QUESTION
Explain why high-carbon steel is used for drill bits but mild steel for car bodies.
[2 marks]
Notes: MARK SCHEME — Recap 3 (total 8 marks) Q1 [2]: Copper is a very good electrical conductor / ductile (1); PVC is an electrical insulator / flexible, so the cable is safe to touch (1). Q2 [2]: A mixture of a metal with other elements / metals (1); harder / stronger / resists corrosion / properties can be designed (1). Q3 [2]: 250 × 0.18 (1); = 45 g (1). Q4 [2]: High-carbon steel is very hard (keeps a cutting edge) (1); mild steel is easier to shape / less brittle / can be pressed into panels (1).

## Slide 15
Practical: density by displacement
Specification C4.1.1 • measuring density to compare materials quantitatively
SUGGESTED PRACTICAL
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Practical | 15
Illustrative diagram — balance, 100 cm³ measuring cylinder, thread, samples
10.7 g
1 find the mass on a balance
2 read V₁ = 50.0 cm³
3 lower sample; read V₂ = 54.0 cm³
thread
Read the bottom of the meniscus at eye level
Method
Measure the mass of the dry sample on a balance (g).
Half-fill a measuring cylinder with water; read the volume V₁ at eye level.
Tie thread to the sample and lower it gently until fully under water; read V₂.
Volume of sample = V₂ − V₁ (cm³). Density = mass ÷ volume. Repeat with different sized pieces of each material.
IV: material. DV: density. Control: same cylinder, water at room temperature, no air bubbles.
Safety: low hazard. Glass cylinders can break: keep away from the bench edge; lower samples gently. Wipe up spills (slip risk). Cut metal samples may have sharp edges.
Worked example: one aluminium piece
Mass 10.7 g; V₁ = 50.0 cm³; V₂ = 54.0 cm³.
1 Volume 54.0 − 50.0 = 4.0 cm³
2 Density 10.7 ÷ 4.0 = 2.675 g/cm³
3 Answer 2.7 g/cm³ (2 s.f.)
Quick check Why must the sample be fully under water? How would you measure the density of a poly(ethene) sample, which floats?
Notes: QUICK CHECK ANSWER: Otherwise only part of its volume displaces water, so V₂ − V₁ is too small and the density is too high. For a floating sample: attach a sinker (e.g. a steel bolt); measure the volume of the sinker alone, then sinker + sample, and subtract; or push it under with a thin wire. Suggested practical: no OCR PAG code is linked to C4.1 in any source found (PAG numbering for J260 chemistry is UNVERIFIED). Regular solids can also be measured with a ruler (V = l × w × h, as for the brick on slide 9). A displacement (eureka) can is an alternative for larger samples. CLEAPSS-style risk: no hazardous chemicals; main risks are broken glass and slips.

## Slide 16
Practical: results and analysis
Specification C4.1.1 • mass against volume; density from the gradient
SUGGESTED PRACTICAL
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Practical | 16
Illustrative diagram — plotted to scale from the table; best-fit lines through the origin (illustrative data)
0
2
4
6
8
10
0
10
20
30
40
50
60
70
80
Volume / cm³
Mass / g
steel
aluminium
nylon
Δx = 6.0 cm³
Δy = 46.9 g
Volume / cm³ | 2.0 | 4.0 | 6.0 | 8.0
Steel mass / g | 15.7 | 31.0 | 47.0 | 62.5
Al mass / g | 5.5 | 10.7 | 16.3 | 21.5
Nylon mass / g | 2.3 | 4.6 | 6.8 | 9.3
Worked example: density from the gradient
Steel line, using the triangle.
1 Gradient Δy ÷ Δx = 46.9 ÷ 6.0
2 Answer = 7.8 g/cm³; aluminium 2.7, nylon 1.15 g/cm³
Errors and improvements
Cylinder read to ±0.5 cm³: for 4.0 cm³ that is ±12.5%; for 8.0 cm³ only ±6.25%. Use bigger samples or a narrower cylinder.
Air bubbles or water lost by splashing; wet samples weighed. Repeat and find a mean; use the gradient of many points.
Quick check Use the table to calculate the density of the 6.0 cm³ steel sample. Why is a line of best fit better than one reading?
Notes: QUICK CHECK ANSWER: 47.0 ÷ 6.0 = 7.83 → 7.8 g/cm³ (2 s.f.). A best-fit line uses all the results, so random errors in single readings average out; it also shows any anomalous result. Illustrative results. Node: least-squares gradients through the origin: steel 7.812, aluminium 2.697, nylon 1.152 g/cm³. Gradient triangle on the best-fit steel line from 2.0 to 8.0 cm³: Δy = 46.9 g, /6.0 = 7.8. Uncertainty: ±0.5 cm³ ÷ 4.0 cm³ = 12.5%; ÷ 8.0 cm³ = 6.25%. Mass and volume have proportional relationship (line through origin) because density is constant for one material.

## Slide 17
Exam practice: recap 4
Specification C4.1.1 • density practical
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Recap 4 | 17
EXAM-STYLE QUESTION
A sample has mass 23.0 g. The water level rises from 50.0 to 58.5 cm³. Calculate the density (2 s.f.).
[2 marks]
EXAM-STYLE QUESTION
Describe how to read the volume of water in a measuring cylinder accurately.
[2 marks]
EXAM-STYLE QUESTION
Explain why using a larger sample makes the density measurement more accurate.
[2 marks]
EXAM-STYLE QUESTION
Mass is plotted against volume for one material. Describe the graph and say what the gradient shows.
[2 marks]
Notes: MARK SCHEME — Recap 4 (total 8 marks) Q1 [2]: Volume = 58.5 − 50.0 = 8.5 cm³ (1); 23.0 ÷ 8.5 = 2.7 g/cm³ (1). Q2 [2]: Eye level with the surface (1); read the bottom of the meniscus (1). Q3 [2]: The reading error / uncertainty of the cylinder (±0.5 cm³) stays the same (1); so it is a smaller percentage of a larger volume (1). Q4 [2]: A straight line through the origin (mass proportional to volume) (1); gradient = density (1).

## Slide 18
Evaluating a choice: car panels
Specification C4.1.2 • weighing benefits against costs using data
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
C4.1.2 | 18
Illustrative diagram — bar charts drawn to scale from the table (illustrative values)
Mass / kg
Cost / £
Steel
Steel
Al
Al
CFRP
CFRP
12
6
4.8
£12
£18
£96
Panel mass
Material cost
Each panel has the same stiffness. Lighter panels → less fuel or longer battery range.
Panel | Mass / kg | £ per kg | Other points
Steel | 12.0 | 1 | cheap, easy to press and repair; can rust
Aluminium | 6.0 | 3 | does not rust; harder to weld
CFRP | 4.8 | 20 | lightest; slow to make; hard to repair
Worked example: percentage mass saved
Replace the 12.0 kg steel panel with a 4.8 kg CFRP panel.
1 Saved 12.0 − 4.8 = 7.2 kg
2 Answer 7.2 ÷ 12.0 × 100 = 60% lighter, but costs £96 not £12
Making a judgement
Family car: steel or aluminium (cost matters). Sports car: CFRP (mass matters most).
A full judgement also looks at energy and waste over the product's whole life: life-cycle assessment (C4.4).
Quick check Calculate the extra cost per kg of mass saved for aluminium compared with steel. Which panel would you choose for a taxi? Why?
Notes: QUICK CHECK ANSWER: Extra cost £18 − £12 = £6 for 12.0 − 6.0 = 6.0 kg saved → £1 per kg saved (CFRP: £84 ÷ 7.2 kg = £11.67 per kg). Taxi: steel or aluminium: cheap to buy and repair, still reasonably light; aluminium does not rust and saves fuel over many miles. Accept a justified answer. All masses and prices are illustrative (asserted in node). C4.1.2 select appropriate materials given details of the usage required. Life-cycle assessment belongs to C4.4 and is mentioned only. IaS: decisions weigh benefits, costs and risks for different people.

## Slide 19
Exam practice: recap 5
Specification C4.1.2 • evaluating material choices
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Recap 5 | 19
EXAM-STYLE QUESTION
A 20 kg steel bonnet is replaced with a 14 kg aluminium one. Calculate the percentage mass saved.
[2 marks]
EXAM-STYLE QUESTION
Give one advantage and one disadvantage of CFRP compared with steel for car panels.
[2 marks]
EXAM-STYLE QUESTION
Suggest why aluminium alloy, not pure aluminium, is used for aircraft bodies.
[2 marks]
EXAM-STYLE QUESTION
Explain why there is rarely a perfect material for a product.
[2 marks]
Notes: MARK SCHEME — Recap 5 (total 8 marks) Q1 [2]: (20 − 14) ÷ 20 × 100 (1); = 30% (1). Q2 [2]: Advantage: lower density / lighter / does not rust / strong for its mass (1). Disadvantage: expensive / hard to repair / slow to make / hard to recycle (1). Q3 [2]: Pure aluminium is soft / weak (1); the alloy is stronger / harder while still low density (1). Q4 [2]: Each material has advantages and disadvantages / no material has every property needed (1); so designers choose the best compromise, e.g. trade mass against cost (1).

## Slide 20
Summary: key words
C4.1 How is data used to choose a material for a particular use? • learn these definitions
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Key words | 20
Ceramic
Hard, brittle, heat-resistant material such as glass, brick or pottery.
Polymer
Material made of very long chain molecules, e.g. poly(ethene).
Composite
Two or more materials combined, e.g. carbon fibres in resin.
Alloy
A mixture of a metal with other elements, e.g. steel.
Steel
Alloy of iron with a small amount of carbon (and sometimes other metals).
Stainless steel
Iron with chromium and nickel: does not rust.
Density
Mass per unit volume: density = mass ÷ volume (g/cm³).
Tensile strength
Force per unit area needed to break a material by pulling it.
Compression
A squashing force; concrete and brick are strong in compression.
Stiffness
How hard it is to bend or stretch a material. Opposite: flexible.
Hardness
How hard it is to scratch or dent the surface.
Brittle
Breaks suddenly without bending first, e.g. glass.
Softening temperature
Temperature at which a polymer becomes soft and can be reshaped.
Conductor
Lets electricity (or heat) pass through easily, e.g. copper.
Specification
A list of what a product (and its material) must do.
Displacement
Finding volume from the rise in water level when an object is submerged.
Notes: Use as a cover-and-recall activity. "Softening temperature" and the property words come from C4.1.1. Bonding words (delocalised electrons, intermolecular forces, giant covalent) belong to C4.2.

## Slide 21
Full exam question
Specification C4.1.1–C4.1.3 • answer every part • 13 marks
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Full question | 21
A company is choosing a material for a ladder. Each ladder uses 250 cm³ of material. Data: aluminium alloy density 2.7 g/cm³; steel density 7.8 g/cm³; GRP is an electrical insulator.
(a) Calculate the mass of the aluminium alloy ladder.
[2 marks]
(b) The steel ladder has a mass of 1950 g. Calculate how much lighter (as a percentage) the aluminium ladder is. (2 s.f.)
[2 marks]
(c) Describe how you could measure the density of a small piece of the alloy in the lab.
[3 marks]
(d) Steel is an alloy of iron. State what is added to iron to make steel, and why.
[2 marks]
(e) Suggest why electricians use GRP ladders rather than aluminium ladders.
[2 marks]
(f) Glass is not used for ladders even though it is hard and strong in compression. Explain why.
[2 marks]
Total: 13 marks
Notes: MARK SCHEME — full question (total 13 marks) (a) [2]: 250 × 2.7 (1); = 675 g (1). (b) [2]: (1950 − 675) ÷ 1950 × 100 (1); = 65% (1). Allow ecf from (a). (c) [3]: Measure mass on a balance (1); find volume by displacement: lower into a measuring cylinder of water and find the rise in level (1); density = mass ÷ volume (1). (d) [2]: Carbon (small amount) (1); makes it harder / stronger than pure iron (1). (e) [2]: GRP is an electrical insulator (1); aluminium conducts, so there is a risk of electric shock near live wires (1). (f) [2]: Glass is brittle / weak in tension / shatters (1); a ladder bends and is knocked, so it would break suddenly / dangerous (1).

## Slide 22
Homework
C4.1 Choosing materials • 17 marks • about 30 minutes
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Homework | 22

## Slide 23
Homework
Answer in full sentences • show all working • 17 marks
OCR GCSE Twenty First Century Science — Combined Science B (J260) | C4.1 How is data used to choose a material for a particular use? | Higher & Foundation
Homework | 23
Answer all questions. Q7 is a 6-mark extended answer: use the data table from slide 8.
1 Name the family of materials that glass and brick belong to.
[1 mark]
2 A metal sample has mass 88.0 g and volume 11.0 cm³. Calculate its density.
[2 marks]
3 22-carat gold contains 22 parts gold in 24. Calculate the percentage of gold (3 s.f.).
[2 marks]
4 A bronze bell of mass 5.0 kg is 12% tin. Calculate the mass of tin.
[2 marks]
5 Explain why polymers are used to make plastic bottles but not saucepan bodies.
[2 marks]
6 Explain why reinforced concrete is a composite and why it is better than concrete alone for a beam.
[2 marks]
7 Use the data on steel, aluminium alloy and CFRP to evaluate which material is best for a bicycle frame.
[6 marks]
Notes: MARK SCHEME — homework (total 17 marks) 1 [1]: Ceramics (1). 2 [2]: 88.0 ÷ 11.0 (1); = 8.0 g/cm³ (1). 3 [2]: 22 ÷ 24 × 100 (1); = 91.7% (1). 4 [2]: 5.0 × 0.12 (1); = 0.6 kg / 0.60 kg / 600 g (1). 5 [2]: Polymers are light / tough / easy to mould / waterproof, good for bottles (1); low softening temperature / poor heat conductor, so would melt on a hob (1). 6 [2]: Steel bars combined with concrete: two materials combined (1); steel is strong in tension, concrete only in compression, so the beam does not crack when it bends (1). 7 [6]: OCR level-of-response mark scheme (6 marks). Read the whole answer, decide the level from the content descriptor, then the mark within the level from the quality of the line of reasoning. Use the indicative scientific points below. Level 3 (5–6 marks): Compares at least TWO materials using properties AND data from the table, AND makes a justified choice for a stated use, considering at least one drawback. There is a well-developed line of reasoning which is clear and logically structured. The information presented is relevant and substantiated. Level 2 (3–4 marks): Compares properties of two materials with some use of data OR makes a choice with a simple reason. There is a line of reasoning presented with some structure. The information presented is relevant and supported by some evidence. Level 1 (1–2 marks): Simple statements, e.g. "carbon fibre is light" or "steel is strong". There is an attempt at a logical structure with a line of reasoning. The information is in the most part relevant. 0 marks: no response or no response worthy of credit. Indicative scientific points may include: • Steel: strong, stiff, cheap, easy to shape and weld; high density (7.8 g/cm³) so heavy; rusts unless painted or stainless. • Aluminium alloy: low density (2.7 g/cm³), does not rust, reasonably strong; more expensive than steel. • CFRP: lowest density (1.6 g/cm³) and highest strength for its mass; very expensive, hard to repair or recycle. • Use data: e.g. same volume (400 cm³) gives 3.12 kg, 1.08 kg and 0.64 kg frames; strength ÷ density 51, 111, 625. • Link properties to the use: a racing bike needs low mass; a commuter bike needs low cost, toughness, easy repair. • Judgement: e.g. CFRP for racing, steel or aluminium for everyday use; justified with data and trade-offs.