## Slide 1
OCR GCSE COMBINED SCIENCE B (TWENTY FIRST CENTURY)
P6.3 Materials under stress
Stretching, compressing and bending; springs, F = kx and elastic energy
Elastic • Plastic • Extension • Spring constant • Limit of proportionality • Elastic energy
§
Specification P6.3.1–P6.3.7 • PAG P2 forces: the force–extension investigation for a spring
H
Higher & Foundation in one deck • no Higher-only statements found in P6.3 • stretch items marked
k
More than one force • elastic and plastic • F = kx • limit of proportionality • E = ½kx²
Part 3 of 3 in Chapter P6: Matter – models and explanations
OCR J260 Combined Science B • P6.3 How does the particle model relate to material under stress? • teacher deck • mark schemes in the speaker notes
Notes: P6.3 How does the particle model relate to material under stress? is Part 3 of 3 in J260 Chapter P6 (P6.1, P6.2, P6.3) and the last physics sub-topic in Combined Science B (chapters P1–P6; there is no P7). The P4 decks in this series left Hooke's law and springs (P4.1) and elastic energy (P4.4) to this sub-topic, so they are taught in full here. Spec wording and numbering in this deck were reconstructed from search extracts and memory because ocr.org.uk could not be fetched: see SPEC_P6_3.md before showing codes to students.

## Slide 2
Learning objectives
Specification P6.3.1–P6.3.7 • by the end of this sub-topic you can…
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Objectives | 2
1
P6.3.1 Explain that to stretch, compress or bend an object, more than one force has to be applied.
2
P6.3.2 Describe the difference between elastic and plastic deformation, and explain it with the particle model.
3
P6.3.3 Describe the relationship between force and extension for a spring and other simple systems.
4
P6.3.4 Describe the difference between linear and non-linear force–extension relationships; the limit of proportionality.
5
P6.3.5 Recall and apply F = k × x and calculate a spring constant in linear cases.
6
P6.3.6 Calculate the work done in stretching from the area under the force–extension graph.
7
P6.3.7 Apply E = ½ × k × x² to find the energy stored in a stretched spring.
8
PAG P2 Practical: investigate how the extension of a spring depends on the force applied.
Notes: No P6.3 statement was found to be Higher tier only (bold) in the J260 specification (UNVERIFIED: check the spec). All objectives are for both tiers; rearranging E = ½kx² and the area under a curved graph are marked GRADE 7–9 STRETCH. Numbering P6.3.1–P6.3.7 is reconstructed (see SPEC_P6_3.md): check against the OCR J260 specification before using codes with students.

## Slide 3
Where this fits
Chapter P6 Matter – models and explanations • P6.3 is Part 3 of 3 in Combined Science B
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Context | 3
P6.3
Materials under stress
P6.3.1 Stretching, compressing and bending need more than one force
BOTH TIERS
P6.3.2 Elastic and plastic deformation; the particle model
BOTH TIERS
P6.3.3–P6.3.5 Force–extension, F = k × x, limit of proportionality
BOTH TIERS
P6.3.6–P6.3.7 Work done = area under the graph; E = ½kx²
BOTH TIERS
PAG P2 Practical: force and extension of a spring; k and energy
PRACTICAL
Earlier links: P4 forces (resultant force, weight W = mg, work done W = Fd) • P6.1 particle model • P2 energy stores
Chapter P6 in J260
P6.1 How does energy transform matter? Density, specific heat capacity, latent heat.
P6.2 How does the particle model explain the effects of heating? Gas particles, temperature and pressure.
P6.3 How does the particle model relate to material under stress? (this deck)
P6.3 is the last physics sub-topic in J260 (chapters P1–P6).
One deck for both tiers
Every slide is for both tiers: no P6.3 statement was found to be Higher only.
F = k × x must be recalled; E = ½ × k × x² is given on the equation sheet.
One practical: PAG P2 (forces): stretching a spring.
Notes: J260 Chapter P6 has three sub-topics in Combined Science: P6.1, P6.2 and P6.3 (see SPEC_P6_1.md). P6.4 (pressure in fluids) and P6.5 (Big Bang) are Physics B (J259) only. J260 physics has chapters P1–P6 only (the J260/03 and /07 examiners' reports describe the papers as testing chapters P1–P6), so this deck completes J260 physics. The P4 decks were lost; in the earlier series P4.1 left Hooke's law and springs to P6.3 and P4.4 left elastic energy to P6.3. This deck therefore teaches F = kx and E = ½kx² from scratch. PAG link: OCR PAG 2 (Forces) "Investigating the effect of forces on springs" (PMT OCR B PAG 2 notes; search extract). Its placement in P6.3 is the natural home but UNVERIFIED against the outline scheme of work.

## Slide 4
Retrieval starter
Recall from P4, P6.1, P2 and maths • 6 minutes • no notes
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Starter | 4
1
P4 • resultant force
A box has 12 N acting to the right and 5 N acting to the left. Give the size and direction of the resultant force.
2
P4 • weight
Calculate the weight of a 0.20 kg mass. (g = 10 N/kg)
3
P4 • work done
A 5.0 N force pulls a box 0.40 m. Calculate the work done.
4
P6.1 • particle model
Describe the arrangement and movement of the particles in a solid.
5
P2 • energy stores
A catapult's elastic band is pulled back. Name the energy store that increases.
6
Maths • units
Convert 35 cm into metres and 2.5 kN into newtons.
Self-mark Swap and mark from the answers. 6/6 secure • 4–5 nearly there • 0–3 revisit the topic notes
Notes: ANSWERS 1. 7 N to the right. 2. W = m × g = 0.20 × 10 = 2.0 N. 3. W = F × d = 5.0 × 0.40 = 2.0 J. 4. Regular pattern / fixed positions, touching; they vibrate about fixed positions. 5. Elastic (potential) energy store. 6. 0.35 m; 2500 N.

## Slide 5
Changing shape needs more than one force
Specification P6.3.1 • stretching, compressing and bending
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
P6.3.1 | 5
Illustrative diagram — force arrows show the forces acting on each object
Stretching
pull
pull
Compressing
push
push
Bending
push
support forces from both ends
Why one force is not enough
To stretch, compress or bend an object, more than one force must act on it, at different places.
With only one force there is a resultant force, so the object just accelerates instead of changing shape.
A spring held at the top: the load pulls down, the clamp pulls up.
Bending a plank needs three forces: a push in the middle and a support force at each end.
Think it through
A 200 g mass hangs on a spring. The spring is still. (g = 10 N/kg)
1 Load the weight (0.200 × 10 = 2 N) pulls the bottom of the spring down
2 Clamp pulls the top of the spring up with 2.0 N
3 Balanced resultant force = 0, so no acceleration
4 Answer two forces at the two ends → the spring stretches
Quick check Explain why you cannot squash a ball of modelling clay with just one force.
Notes: QUICK CHECK ANSWER: One force on its own gives a resultant force, so the clay would accelerate/move in that direction. To squash it you need two forces in opposite directions on different parts (e.g. two hands, or a hand and the table). Demo: pull one end of a spring lying on a smooth bench – it slides rather than stretches. Then hold the other end.

## Slide 6
Elastic and plastic deformation
Specification P6.3.2 • does the object go back to its original shape?
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
P6.3.2 | 6
Illustrative diagram — the same kind of spring before, during and after loading
original
length
1 No load
2 Load added:
stretches
3 Load removed:
same length
4 Overstretched,
load removed:
stays longer
ELASTIC
PLASTIC
Two kinds of deformation
Elastic deformation: the object goes back to its original shape and size when the forces are removed (a spring or rubber band used gently).
Plastic deformation: the object is permanently changed; it does not go back when the forces are removed (modelling clay, a bent paper clip).
If a spring is stretched too far it passes its elastic limit and then deforms plastically.
Test: remove the load and measure the length again.
Sort the examples
Decide whether each deformation is elastic or plastic.
1 Trampoline springs return to shape → elastic
2 Crushed can stays crushed → plastic
3 Bow string returns when released → elastic
4 Answer elastic = returns to shape; plastic = permanent change
Quick check A car bumper dents in a crash and stays dented. Is this elastic or plastic deformation? Give a reason.
Notes: QUICK CHECK ANSWER: Plastic – the bumper does not return to its original shape when the force is removed. OCR uses "elastic" and "plastic" deformation (students may also meet "inelastic" from other boards).

## Slide 7
The particle model of stretching
Specification P6.3.2 • forces between particles change when their separation changes
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
P6.3.2 | 7
Illustrative diagram — particles in a solid joined by forces, drawn as tiny springs (NOT to scale)
A No force
B Stretched
further apart: attraction pulls back
C Compressed
closer together: repulsion pushes back
D Plastic: layers slip
new neighbours: stays deformed
Explaining elastic and plastic
Particles in a solid are held in place by forces between them (bonds).
Stretching pulls particles slightly further apart: attractive forces pull them back. Compressing pushes them closer: repulsive forces push back.
Elastic: remove the force and the particles return to their original positions.
Plastic: a large force makes layers of particles slide to new positions. They bond to new neighbours, so they stay there.
Use the model
Why does a stretched spring pull back on your hand?
1 Stretch the separation of the particles increases
2 Forces attraction between particles pulls them back together
3 Spring these forces add up along the spring
4 Answer the spring exerts a force back towards its original length
Quick check Use the particle model to explain why a paper clip stays bent after you bend it a long way.
Notes: QUICK CHECK ANSWER: The large force made layers of particles slide past each other to new positions (1); the particles form bonds with new neighbours, so they do not return when the force is removed – plastic deformation (1). Spec link: the OCR B background to 6.3 says compressing or stretching changes the separation of the particles and the forces between them (docbrown J259/J260 extract). The "slip" picture is a simple model of plastic flow (dislocations are not required).

## Slide 8
Exam practice: recap 1
Specification P6.3.1–P6.3.2 • forces and deformation
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Recap 1 | 8
EXAM-STYLE QUESTION
Explain why two forces are needed to stretch an elastic band.
[2 marks]
EXAM-STYLE QUESTION
Describe the difference between elastic and plastic deformation. Give one example of each.
[3 marks]
EXAM-STYLE QUESTION
Use the particle model to explain why a stretched wire pulls back when it is stretched a small amount.
[2 marks]
Notes: MARK SCHEME — Recap 1 (total 7 marks) Q1 [2]: One force alone gives a resultant force so the band accelerates/moves (1); two forces in opposite directions at different points stretch it / change its shape (1). Q2 [3]: Elastic: returns to original shape/length when the force is removed (1); plastic: permanent change / does not return (1); one correct example of each, e.g. spring used gently / modelling clay (1). Q3 [2]: Particles are pulled further apart / separation increases (1); attractive forces between particles pull them back towards their original positions (1).

## Slide 9
Force and extension: F = k × x
Specification P6.3.3, P6.3.5 • recall and apply the spring equation in linear cases
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
P6.3.5 | 9
Illustrative diagram — extension = new length − original length
original
length
x
extension
F (weight of load)
no load
F = k × x
RECALL
The spring equation
F = k × x (RECALL). F in N, x in m, k in N/m.
Extension x = new length − original length. Convert cm to m: ÷ 100.
The spring constant k measures stiffness: a stiffer spring has a bigger k and needs more force for each metre of extension.
It only works while F and x are directly proportional (a linear system).
Worked example
A 3.0 N force stretches a spring by 12 cm. Calculate the spring constant.
1 Equation F = k × x
2 Rearrange k = F ÷ x
3 Substitute k = 3.0 N ÷ 0.12 m
4 Answer k = 25 N/m
Quick check A spring has k = 40 N/m. What force stretches it by 5.0 cm? What extension would a 3.0 N force give?
Notes: QUICK CHECK ANSWER: F = 40 × 0.050 = 2.0 N. x = F ÷ k = 3.0 ÷ 40 = 0.075 m (7.5 cm). F = k × x is a RECALL equation (national list: force exerted by a spring = extension × spring constant). Rearranging is expected at both tiers here because it is a simple two-term rearrangement.

## Slide 10
Linear and non-linear force–extension graphs
Specification P6.3.3, P6.3.4 • the limit of proportionality
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
P6.3.4 | 10
Illustrative diagram — to scale: a spring with k = 40 N/m, and a rubber band (non-linear)
0.00
0.05
0.10
0.15
0.20
0.25
0.30
0
1
2
3
4
5
6
7
8
9
extension / m
force / N
limit of proportionality
linear
spring: curves
rubber band
Reading the graph
Linear: a straight line through the origin, so F ∝ x. Double the force → double the extension.
With force on the y-axis, the gradient = spring constant k.
Limit of proportionality: the point beyond which F and x are no longer proportional; the line curves.
Non-linear: equal force steps do not give equal extensions, so F = k × x does not apply. A rubber band is elastic but non-linear.
Worked example: k from the graph
Use the straight part of the spring line.
1 Read at x = 0.10 m, F = 4.0 N
2 Equation k = F ÷ x (= gradient)
3 Substitute k = 4.0 N ÷ 0.10 m
4 Answer k = 40 N/m
Quick check Use the graph: what force gives an extension of 0.05 m on the spring? What is the force at its limit of proportionality?
Notes: QUICK CHECK ANSWER: 2.0 N (F = 40 × 0.05); limit of proportionality at 6 N (x = 0.15 m). Graph drawn to scale: spring F = 40x to (0.15 m, 6.0 N), then curving (extension increases more for each extra newton). Rubber band drawn as F = 100x² (illustrative: real rubber is more complicated, but the key point is that it is elastic yet non-linear). The limit of proportionality is not always the same point as the elastic limit (the spring can still be elastic a little beyond it).

## Slide 11
Exam practice: recap 2
Specification P6.3.3–P6.3.5 • F = k × x and force–extension graphs
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Recap 2 | 11
EXAM-STYLE QUESTION
A force of 6.0 N stretches a spring by 15 cm. Calculate the spring constant. Give the unit.
[3 marks]
EXAM-STYLE QUESTION
Describe how a force–extension graph shows that a spring is linear, and how you would find the limit of proportionality.
[2 marks]
EXAM-STYLE QUESTION
A spring has a spring constant of 50 N/m. Calculate its extension when a 2.0 N force is applied. Give your answer in cm.
[2 marks]
Notes: MARK SCHEME — Recap 2 (total 7 marks) Q1 [3]: k = F ÷ x (1); = 6.0 ÷ 0.15 (1); = 40 N/m (1, unit needed). Q2 [2]: Straight line through the origin / F directly proportional to x (1); the limit of proportionality is where the line stops being straight / starts to curve (1). Q3 [2]: x = F ÷ k = 2.0 ÷ 50 = 0.040 m (1); = 4.0 cm (1).

## Slide 12
Work done in stretching a spring
Specification P6.3.6, P6.3.7 • energy stored = area under the force–extension graph
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
P6.3.6 | 12
Illustrative diagram — shaded area = work done = energy stored (k = 40 N/m)
0.00
0.05
0.10
0.15
0.20
0
1
2
3
4
5
6
7
8
extension / m
force / N
area = ½ × F × x
(0.15 m, 6.0 N)
Energy stored in a stretched spring
You do work to stretch a spring. If the deformation is elastic, the energy is stored in its elastic energy store, and is given back when it is released.
E = ½ × k × x² (GIVEN on the equation sheet).
Work done = area under the force–extension graph. In the linear part this is a triangle: ½ × F × x.
Why ½? The force rises from 0 to F, so the average force is ½F.
Worked example
The spring (k = 40 N/m) is stretched by 0.15 m. Calculate the energy stored.
1 Equation E = ½ × k × x²
2 Substitute E = 0.5 × 40 × 0.15²
3 Check area = ½ × 6.0 N × 0.15 m
4 Answer E = 0.45 J
Quick check A spring with k = 200 N/m is stretched by 5.0 cm. Calculate the energy stored.
Notes: QUICK CHECK ANSWER: E = 0.5 × 200 × 0.050² = 0.25000000000000006 J. Common errors: forgetting to square x; squaring (k × x); leaving x in cm. E = ½kx² is GIVEN on the J260 equation sheet ("energy stored in a stretched spring = ½ × spring constant × (extension)²" appears on the OCR B data sheet in third-party copies of J259 papers). In P4.4 of this series elastic energy was left to P6.3.

## Slide 13
Energy beyond the limit of proportionality
Specification P6.3.6, P6.3.7 • rearranging E = ½kx² and counting squares
GRADE 7–9 STRETCH
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
P6.3.6 stretch | 13
Illustrative diagram — area under the whole curve, estimated by counting squares
0.00
0.05
0.10
0.15
0.20
0.25
0.30
0
1
2
3
4
5
6
7
8
9
extension / m
force / N
1 square = 0.05 m × 1 N = 0.05 J
Two Grade 7–9 skills
Rearranging E = ½kx²: x² = 2E ÷ k, so x = √(2E ÷ k). Take the square root last.
Beyond the limit of proportionality E = ½kx² does not apply: use the area under the curve.
Count squares: about 32 squares × 0.05 J ≈ 1.6 J up to 0.30 m.
Count part-squares as halves. State the value of one square first.
Worked example (rearranging)
A spring with k = 40 N/m stores 0.20 J. Calculate its extension.
1 Equation E = ½ × k × x²
2 Rearrange x = √(2E ÷ k)
3 Substitute x = √(2 × 0.20 ÷ 40) = √0.010
4 Answer x = 0.10 m (10 cm)
Quick check A spring with k = 50 N/m stores 1.0 J of energy. Calculate its extension.
Notes: QUICK CHECK ANSWER: x = √(2 × 1.0 ÷ 50) = √0.040 = 0.20 m. Area under the curve computed numerically in node: 1.578 J = 31.6 squares of 0.05 J (accept 1.5–1.7 J). The linear part alone (to 0.15 m) is 0.45 J = 9 squares. No P6.3 statement was found to be HT; this is extension material (spec: "calculate the work done ... by calculating the appropriate area on the force–extension graph" – the area method applies to non-linear systems too).

## Slide 14
Exam practice: recap 3
Specification P6.3.6–P6.3.7 • work done and energy stored
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Recap 3 | 14
EXAM-STYLE QUESTION
A spring has a spring constant of 30 N/m. It is stretched by 0.20 m. Calculate the energy stored. Use E = ½ × k × x².
[2 marks]
EXAM-STYLE QUESTION
A force–extension graph is a straight line from the origin to 4.0 N at 0.080 m. Use the graph to calculate the work done stretching the spring.
[2 marks]
EXAM-STYLE QUESTION
Stretch: a spring with spring constant 50 N/m stores 0.36 J. Calculate its extension.
[3 marks]
Notes: MARK SCHEME — Recap 3 (total 7 marks) Q1 [2]: E = 0.5 × 30 × 0.20² (1); = 0.60 J (1). Q2 [2]: Area of triangle = ½ × 4.0 × 0.080 (1); = 0.16 J (1). Q3 [3]: x² = 2E ÷ k (1); = 2 × 0.36 ÷ 50 = 0.0144 (1); x = 0.12 m (1).

## Slide 15
PAG P2: force and extension of a spring
Specification P6.3.3 • apparatus and method
PAG P2
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
PAG P2 | 15
Illustrative diagram — clamp stand, spring, metre rule, pointer and slotted masses
spring
metre rule
pointer
slotted masses
clamp stand
G-clamp
Method
Clamp the spring and a vertical metre rule to the stand. Fix a pointer to the bottom of the spring.
Record the pointer reading with no load: the original length.
Add a 100 g mass (weight 1.0 N). Read the new length with your eye level with the pointer.
Repeat, adding 1.0 N each time, up to 7 N. Extension = length − original length.
Unload one mass at a time to check the spring returns to its original length (elastic).
Plot force (y-axis) against extension (x-axis) and draw a line of best fit.
Tips for accurate results
1 Zero measure the original length before loading
2 Eye level avoids parallax error
3 Wait let the spring stop bouncing before reading
4 Answer check the rule is vertical with a set square
Quick check A 100 g mass is added each time. Show that each mass adds a force of 1.0 N. (g = 10 N/kg)
Notes: QUICK CHECK ANSWER: W = m × g = 0.100 kg × 10 N/kg = 1.0 N. Equipment: clamp stand, two bosses and clamps, G-clamp, spring, metre rule, pointer (e.g. a splint taped to the spring), 100 g mass hanger and slotted masses, safety goggles. PAG P2 (OCR Forces group): "Investigating the effect of forces on springs" (PMT OCR B PAG 2 notes, search extract). OCR's second suggested activity (determining the work done in stretching safely) is covered by the graph-area analysis on the next slides.

## Slide 16
PAG P2: variables and safety
Specification P6.3.3 • planning a fair test
PAG P2
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
PAG P2 | 16
Illustrative diagram — what you change, measure and keep the same
Independent variable (you change)
force on the spring (weight of the masses, N)
Dependent variable (you measure)
extension of the spring (m), from the length readings
Control variables (keep the same)
the same spring • rule fixed in the same place • same size of mass steps
Analysis plan
Find k from the gradient of the straight part of the graph.
Find the work done from the area under the graph (or E = ½kx² in the linear part).
Mark the limit of proportionality, where the line starts to curve.
Safety
Hazard → risk → control
1 Masses could fall on feet → keep feet clear; tray or cushion below
2 Spring could snap back into eyes → wear safety goggles
3 Stand could topple → clamp it to the bench with a G-clamp
4 Answer do not overload: stop when the spring stays stretched
Quick check Name the independent variable and the dependent variable in this investigation.
Notes: QUICK CHECK ANSWER: Independent = force (weight added); dependent = extension. Control: same spring (same material, coil diameter, number of coils), same temperature, rule kept vertical and fixed.

## Slide 17
PAG P2: results and graph
Specification P6.3.3, P6.3.4 • sample results for one spring (g = 10 N/kg)
PAG P2
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
PAG P2 | 17
Illustrative diagram — sample data plotted to scale; best-fit line through the linear points
0.00
0.05
0.10
0.15
0.20
0.25
0.30
0.35
0.40
0
1
2
3
4
5
6
7
8
extension / m
force / N
limit of
proportionality
Force / N | Length / cm | Extension / cm | Extension / m
0.0 | 5.0 | 0.0 | 0.000
1.0 | 10.1 | 5.1 | 0.051
2.0 | 14.9 | 9.9 | 0.099
3.0 | 20.0 | 15.0 | 0.150
4.0 | 25.1 | 20.1 | 0.201
5.0 | 29.9 | 24.9 | 0.249
6.0 | 35.0 | 30.0 | 0.300
7.0 | 42.5 | 37.5 | 0.375
What the results show
Up to 6.0 N the points lie on a straight line through the origin: F ∝ x (linear).
The 7.0 N point (red) is well off the line: the spring is past its limit of proportionality.
Original length = 5.0 cm. Each extension = length − 5.0 cm.
Quick check Use the table: what is the extension, in metres, when the force is 4.0 N? Does F = k × x with k = 20 N/m fit this point?
Notes: QUICK CHECK ANSWER: 25.1 − 5.0 = 20.1 cm = 0.201 m; yes: 20 × 0.201 = 4.0 N (to 2 s.f.). Sample data: lengths 5, 10.1, 14.9, 20, 25.1, 29.9, 35, 42.5 cm for 0–7 N. Extensions 0, 5.1, 9.9, 15, 20.1, 24.9, 30, 37.5 cm. Least-squares gradient through the origin for 0–6 N = 20.01 N/m (node). Plotted to scale with force on the y-axis.

## Slide 18
PAG P2: spring constant and work done
Specification P6.3.5, P6.3.6 • analysing the graph
PAG P2
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
PAG P2 | 18
Illustrative diagram — gradient triangle and shaded area on the best-fit line
0.00
0.05
0.10
0.15
0.20
0.25
0.30
0.35
0.40
0
1
2
3
4
5
6
7
8
extension / m
force / N
Δx = 0.25 m
ΔF = 5.0 N
area = work done
Finding k and the work done
k = gradient = ΔF ÷ Δx. Use a large triangle on the line of best fit, not two data points.
Gradient = 5.0 N ÷ 0.25 m = 20 N/m.
Work done stretching the spring to 6.0 N = area under the line = ½ × 6.0 N × 0.30 m.
Worked example: work done
Calculate the energy stored when the spring (k = 20 N/m) is stretched by 0.30 m.
1 Equation E = ½ × k × x²
2 Substitute E = 0.5 × 20 × 0.30²
3 Check area = ½ × 6.0 × 0.30 = 0.90 J ✓
4 Answer E = 0.90 J
Quick check Calculate the work done when the same spring is stretched to an extension of 0.20 m.
Notes: QUICK CHECK ANSWER: E = 0.5 × 20 × 0.20² = 0.40 J (or area ½ × 4.0 × 0.20 = 0.40 J). Gradient triangle from (0.05 m, 1.0 N) to (0.30 m, 6.0 N) on the best-fit line.

## Slide 19
PAG P2: errors and improvements
Specification P6.3.3 • evaluating the method
PAG P2
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
PAG P2 | 19
Illustrative diagram — parallax: the reading depends on where your eye is
pointer
too high
eye level ✓
too low
Sources of error
Parallax error: reading from above or below → read at eye level, with the pointer close to the rule.
Rule not vertical → check with a set square or plumb line.
Spring still bouncing → wait until it is still before reading.
Zero error: measure extension from the unloaded length, not from 0 on the rule.
Overloading past the elastic limit stretches the spring for good, so later results cannot be repeated.
Improving the investigation
1 Repeat read while loading and unloading; calculate a mean
2 Range use smaller force steps near the limit of proportionality
3 Precision use a rule with mm marks and a fine pointer
4 Answer more points → a more reliable gradient (k)
Quick check A student plots force against length instead of extension. How would the graph look?
Notes: QUICK CHECK ANSWER: Still a straight line (in the linear region) with the same gradient, but it would NOT pass through the origin – it would cross the length axis at the original length (5.0 cm).

## Slide 20
Exam practice: recap 4
Specification P6.3.3–P6.3.6 • PAG P2 springs
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Recap 4 | 20
EXAM-STYLE QUESTION
In the spring investigation, name the independent variable, the dependent variable and one control variable.
[3 marks]
EXAM-STYLE QUESTION
Explain why the student reads the metre rule with their eye level with the pointer.
[1 mark]
EXAM-STYLE QUESTION
On a student's graph, a force of 4.0 N gives an extension of 0.16 m in the linear region. Calculate the spring constant and the work done stretching the spring to this extension.
[4 marks]
Notes: MARK SCHEME — Recap 4 (total 8 marks) Q1 [3]: IV: force/weight/mass added (1); DV: extension (1); CV: same spring / same original length / same temperature (1). Q2 [1]: To avoid parallax error (so the readings are accurate) (1). Q3 [4]: k = 4.0 ÷ 0.16 (1) = 25 N/m (1); work done = ½ × 4.0 × 0.16 or ½ × 25 × 0.16² (1) = 0.32 J (1).

## Slide 21
Summary: key words
P6.3 How does the particle model relate to material under stress? • learn these definitions
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Key words | 21
Deformation
A change of shape: stretching, compressing, bending or twisting.
Stretching
Pulling an object longer: needs forces pulling in opposite directions.
Compressing
Squashing an object shorter: needs forces pushing towards each other.
Bending
Changing shape with forces in more than one place, e.g. push + two supports.
Elastic deformation
The object returns to its original shape when the forces are removed.
Plastic deformation
A permanent change of shape: it does not return when forces are removed.
Elastic limit
The largest force for which deformation is still elastic.
Particle model
Stretching or compressing changes particle separation and the forces between them.
Extension (x)
New length − original length, in m.
Spring constant (k)
Force per metre of extension (N/m); a stiffer spring has a bigger k.
Linear
F ∝ x: a straight line through the origin on a force–extension graph.
Non-linear
Force and extension not proportional: the graph is curved.
Limit of proportionality
The point beyond which F and x are no longer proportional.
Work done
Energy transferred by a force; area under the force–extension graph.
Elastic energy store
Energy stored in a stretched or compressed object: E = ½kx².
Parallax error
A reading error from not having your eye level with the pointer.
Notes: Use as a cover-and-recall activity: hide the definitions, students say them, then reveal.

## Slide 22
Summary: equations
Recall or given? Check against the J260 equation sheet
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Equations | 22
Equation | In words (units) | Recall or given? | Spec
F = k × x | force exerted by a spring (N) = spring constant (N/m) × extension (m) | RECALL | P6.3.5
E = ½ × k × x² | energy stored in a stretched spring (J) = ½ × spring constant (N/m) × (extension (m))² | GIVEN (J260 sheet) | P6.3.7
W = m × g | weight (N) = mass (kg) × gravitational field strength (N/kg) | RECALL | PAG P2
W = F × d | work done (J) = force (N) × distance moved in the direction of the force (m) | RECALL | P6.3.6
Quick check Which equation for springs must you learn by heart? Which one can you look up on the equation sheet?
Notes: QUICK CHECK ANSWER: Learn F = k × x (and W = m × g, W = F × d). E = ½ × k × x² is given on the sheet. Status follows the GCSE subject content equation lists used by J260 (force exerted by a spring = extension × spring constant is recall; energy stored in a stretched spring = ½ × k × x² is on the sheet; third-party copies of J259 papers show it on the OCR B data sheet). UNVERIFIED against the current J260 equation sheet wording: check before printing.

## Slide 23
Full exam question
Specification P6.3.1–P6.3.7 • answer every part • 13 marks
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Full question | 23
A student hangs a spring from a clamp. With no load its length is 8.0 cm. With a load of weight 3.0 N its length is 20.0 cm. The spring is still elastic and obeys F = k × x. (g = 10 N/kg)
(a) Explain why the clamp must exert a force on the spring for it to stretch.
[2 marks]
(b) Calculate the extension in metres, and the spring constant of the spring.
[3 marks]
(c) Calculate the energy stored in the spring. Use E = ½ × k × x².
[2 marks]
(d) Calculate the mass of the load.
[1 mark]
(e) The student adds much more load. When the load is removed, the spring is 10.5 cm long. Name this type of deformation and explain it using the particle model.
[3 marks]
(f) Describe how a force–extension graph for this spring would show the point where it stopped obeying F = k × x.
[2 marks]
Total: 13 marks
Notes: MARK SCHEME — full question (total 13 marks) (a) [2]: Stretching needs more than one force / two forces in opposite directions (1); without the clamp's upward force the resultant force would make the spring and load accelerate/fall rather than stretch (1). (b) [3]: x = 20.0 − 8.0 = 12.0 cm = 0.12 m (1); k = F ÷ x = 3.0 ÷ 0.12 (1); = 25 N/m (1). (c) [2]: E = 0.5 × 25 × 0.12² (1); = 0.18 J (1). ECF from (b). (d) [1]: m = W ÷ g = 3.0 ÷ 10 = 0.30 kg (1). (e) [3]: Plastic deformation (1); layers of particles have slid / moved to new positions (1); bonds formed with new neighbours so particles do not return to original positions (1). (f) [2]: Straight line through origin at first (1); the line curves / stops being straight at the limit of proportionality (1).

## Slide 24
Homework
P6.3 How does the particle model relate to material under stress? • 17 marks • about 30 minutes
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Homework | 24

## Slide 25
Homework
Answer in full sentences • show all working • 17 marks
OCR GCSE Twenty First Century Science — Combined Science B (J260) | P6.3 How does the particle model relate to material under stress? | Higher & Foundation
Homework | 25
All students answer all questions. Q6 is a stretch calculation.
1 Name the type of deformation where an object returns to its original shape when the forces are removed.
[1 mark]
2 A spring has a spring constant of 80 N/m. Calculate the force needed to stretch it by 5.0 cm.
[2 marks]
3 Calculate the energy stored in the spring in Q2. Use E = ½ × k × x².
[2 marks]
4 Describe the difference between a linear and a non-linear force–extension relationship.
[2 marks]
5 Use the particle model to explain why plastic deformation is permanent.
[2 marks]
6 Stretch: 5.0 J of work stretches a spring by 0.20 m. Calculate the spring constant.
[2 marks]
7 Describe how a student could investigate how the extension of a spring depends on the force applied. Include the equipment, the measurements, how to use a graph to find the spring constant and the energy stored, and one safety precaution.
[6 marks]
Notes: MARK SCHEME — homework (total 17 marks) 1 [1]: Elastic (deformation) (1). 2 [2]: F = k × x = 80 × 0.050 (1); = 4.0 N (1). 3 [2]: E = 0.5 × 80 × 0.050² (1); = 0.10 J (1). 4 [2]: Linear: force directly proportional to extension / straight line through the origin (1); non-linear: not proportional / curved graph, e.g. rubber band or a spring beyond its limit of proportionality (1). 5 [2]: Layers of particles slide to new positions (1); they bond to new neighbours, so they do not return when the force is removed (1). 6 [2]: k = 2E ÷ x² = 2 × 5.0 ÷ 0.20² (1); = 250 N/m (1). 7 [6]: OCR level-of-response mark scheme (6 marks). Read the whole answer, decide the level from the content descriptor, then the mark within the level from the quality of the line of reasoning. Use the indicative scientific points below. Level 3 (5–6 marks): Describes a full method including the measurements AND explains how to use the graph to find k AND the energy stored, AND gives a safety precaution. There is a well-developed line of reasoning which is clear and logically structured. The information presented is relevant and substantiated. Level 2 (3–4 marks): Describes a method with most measurements AND EITHER how to find k OR how to find the energy from the graph. There is a line of reasoning presented with some structure. The information presented is relevant and supported by some evidence. Level 1 (1–2 marks): Gives a simple description of adding masses and measuring the spring OR names some equipment. There is an attempt at a logical structure with a line of reasoning. The information is in the most part relevant. 0 marks: no response or no response worthy of credit. Indicative scientific points may include: • Equipment: clamp stand, boss and clamp, spring, metre rule (clamped vertically), pointer, 100 g mass hanger and slotted masses, G-clamp, goggles. • Measure the original (unloaded) length of the spring from the pointer reading. • Add masses in equal steps (e.g. 100 g = 1.0 N); read the new length each time at eye level; wait for the spring to stop moving. • Extension = new length − original length; convert to m; weight W = m × g. • Plot force (y-axis) against extension (x-axis); draw a line of best fit. • Spring constant k = gradient of the straight (linear) part; limit of proportionality where the line curves. • Energy stored / work done = area under the graph (½ × F × x) or E = ½kx² in the linear part. • Safety: goggles in case the spring snaps; keep feet clear / tray under the masses; G-clamp the stand so it does not topple.