## Slide 1
PEARSON EDEXCEL GCSE PHYSICS (1PH0)
Topic 10 Electricity and Circuits
Current, potential difference, resistance, power and mains electricity
Current • Potential difference • Resistance • I–V graphs • Power • Mains
§
Specification 10.1–10.43 • Core Practical 10.17 (electrical circuits)
H
Higher & Foundation in one deck • Grade 7–9 stretch slides are marked
10
Topic 10 of 15 • Paper 2
Pearson Edexcel GCSE (9–1) Physics 1PH0 • teacher deck • mark schemes and answers in the speaker notes
Notes: Topic 10 Electricity and circuits (Paper 2). Every statement 10.1–10.43 is also in Combined Science 1SC0, and no statement in this topic is marked H (Higher only) in our spec check – see SPEC_T10.md for confidence notes. Static electricity is Topic 11 (physics only) and is not in this deck.

## Slide 2
Learning objectives
Specification 10.1–10.43 • by the end of this topic you can…
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Objectives | 2
1
10.1–10.3, 10.10 Describe the atom, draw circuit diagrams with the correct symbols, and compare series and parallel circuits.
2
10.4–10.9 Explain current and potential difference; use Q = I × t and E = Q × V; connect ammeters and voltmeters.
3
10.11–10.16 Use V = I × R; explain the current, p.d. and resistance rules for series and parallel circuits.
4
10.17 Core Practical: construct circuits to investigate V, I and R for a resistor and a filament lamp; test series and parallel circuits.
5
10.18–10.21 Explain I–V graphs for a resistor, filament lamp and diode; describe LDRs and thermistors.
6
10.22–10.26 Explain the heating effect of a current, ways to reduce it, and its advantages and disadvantages.
7
10.27–10.32 Calculate energy and power: E = I × V × t, P = E ÷ t, P = I × V and P = I² × R.
8
10.33–10.43 Explain a.c. and d.c., UK mains (230 V, 50 Hz), live, neutral and earth wires, fuses and power ratings.
Notes: All eight objectives are in both 1PH0 and Combined Science 1SC0. No Topic 10 statement is Higher-only in our spec check (medium confidence – see SPEC_T10.md), so there are no HT pills in this deck. Grade 7–9 stretch content is marked with a red STRETCH pill.

## Slide 3
Where this fits
Specification 10.1–10.43 • Topic 10 is assessed on Paper 2
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Context | 3
Topic 10
Electricity and circuits
10.1–10.3, 10.10 Atoms, circuit symbols, series and parallel
BOTH COURSES
10.4–10.9 Charge, current, p.d.; Q = It, E = QV; meters
BOTH COURSES
10.11–10.16 Resistance, V = IR, series and parallel rules
BOTH COURSES
10.17 Core Practical: electrical circuits
CORE PRACTICAL
10.18–10.21 I–V graphs, diodes, LDRs and thermistors
BOTH COURSES
10.22–10.32 Heating effect, energy and power
BOTH COURSES
10.33–10.43 a.c. and d.c., mains wiring and safety
BOTH COURSES
Earlier links: Topic 1 units • Topic 3 energy stores and efficiency • Topic 6 the atom • Topic 8 power
How this is assessed
1PH0 Paper 2 (2F or 2H): 1 h 45 min, 100 marks, Topics 1 and 8–15.
Combined Science 1SC0 Paper 6 (Physics 2) tests the same Topic 10 statements.
Equations: recall Q = It, E = QV, V = IR, P = E/t, P = IV, P = I²R; given E = IVt.
Core Practical 10.17 can be examined in any style: circuits, method, results and errors.
One deck for both courses and tiers
Combined (1SC0) classes skip nothing: there are no physics-only (P) statements in Topic 10.
No HT pills: our spec check found no Higher-only (H) statements in this topic. Higher students still meet harder calculations.
GRADE 7–9 STRETCH pills mark extension, e.g. total resistance in parallel.
Notes: Physics-only statements: none (all of Topic 10 is shared with 1SC0). Higher-only statements: none found (medium confidence – check the bold H markers in the Pearson spec PDF before publishing; see SPEC_T10.md). Static electricity is Topic 11 (physics only) and magnetism is Topic 12.

## Slide 4
Retrieval starter
Recall from Topics 1, 3, 6, 8 and 15 • 6 minutes • no notes
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Starter | 4
1
Topic 1 • units
Convert 2.5 kW into watts and 3 minutes into seconds.
2
Topic 6 • the atom
Name the three particles in an atom and give the relative charge of each.
3
Topic 3 • energy stores
An electric kettle heats water. Which energy store increases?
4
Topic 3 • efficiency
A motor is supplied with 500 J and transfers 400 J usefully. Calculate its efficiency.
5
Topic 8 • power
A motor does 600 J of work in 20 s. Calculate its power and give the unit.
6
Topic 15 • springs
A spring has k = 50 N/m. Calculate the force needed to stretch it by 0.04 m.
Self-mark Swap and mark from the answers. 6/6 secure • 4–5 nearly there • 0–3 revisit the topic notes
Notes: ANSWERS 1. 2500 W; 180 s. 2. Proton +1, neutron 0, electron −1. 3. The thermal energy store of the water. 4. 400/500 = 0.8 (80%). 5. P = E/t = 600/20 = 30 W. 6. F = k × x = 50 × 0.04 = 2.0 N.

## Slide 5
Circuit symbols
Specification 10.2 • draw and use circuit diagrams
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.2 | 5
Illustrative diagram — standard UK circuit symbols, as used by Edexcel
cell
battery (2 cells)
switch (open)
switch (closed)
filament lamp
fixed resistor
variable resistor
fuse
A
ammeter
V
voltmeter
M
motor
diode
LED
LDR
thermistor
junction (dot)
Drawing conventions
Draw wires as straight lines with square corners; use a ruler.
The long thin line of a cell is the positive (+) terminal.
A dot shows a junction where wires join.
Ammeter: in series. Voltmeter: in parallel across a component.
The diode triangle points in the direction of the conventional current it lets through.
LDR arrows point in (light falls on it); LED arrows point out (it gives out light).
Quick check Draw the symbols for a variable resistor, a thermistor and an LED. How is the LED symbol different from a diode?
Notes: QUICK CHECK ANSWER: see the panel. An LED is a diode with two arrows pointing OUT (it emits light). Spec 10.2 lists cells, batteries, switches, voltmeters, ammeters, resistors, variable resistors, lamps, motors, diodes, thermistors, LDRs and LEDs. The fuse symbol is added for 10.41.

## Slide 6
Series and parallel circuits
Specification 10.3, 10.10 • one loop or several branches
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.3 | 6
Illustrative diagram — the same battery and two identical lamps, connected two ways
Series: one loop
lamp 1
lamp 2
Parallel: two branches
lamp 1
lamp 2
Two ways to connect components
A closed circuit with a source of p.d. (a cell or battery) has a current in it. Open the switch → no current.
Series: components in one loop. The same current passes through each one. One lamp breaks → all go off.
Parallel: components on separate branches, each connected across the supply. Each branch can be switched on its own.
Homes are wired in parallel: each appliance gets the full mains p.d.
Compare the circuits
One lamp “blows” (its filament breaks). What happens to the other lamp?
1 Series the only loop is broken → no current → other lamp goes off
2 Parallel the other branch is still a complete loop → it stays on
3 Why a parallel circuit has more than one path for charge
4 Answer use parallel when devices must work independently
Quick check Fairy lights all go out when one bulb is removed. Are the bulbs in series or parallel? Explain.
Notes: QUICK CHECK ANSWER: Series – removing one bulb breaks the single loop, so there is no current anywhere. 10.10: a closed circuit that includes a source of p.d. has a current in it.

## Slide 7
Charge and current: Q = I × t
Specification 10.1, 10.8, 10.9 • current is the rate of flow of charge
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.8 | 7
Illustrative diagram — not to scale: in a metal wire the free electrons drift through the wire
particle charge mass
proton
+1
1
neutron
0
1
electron
−1
very small
nucleus: protons + neutrons; electrons outside
electron flow
conventional current (+ to −)
metal wire
What is an electric current?
Atoms have a nucleus (protons and neutrons) with electrons around it. Metals have free electrons that can move.
Current is the rate of flow of charge. In metals the charge is carried by electrons.
Q = I × t charge (C) = current (A) × time (s)
RECALL: you must learn this equation.
1 ampere (A) = 1 coulomb of charge passing a point each second.
Worked example
A current of 0.25 A flows through a lamp for 2.0 minutes. Calculate the charge that flows.
1 Equation Q = I × t
2 Convert t = 2.0 × 60 = 120 s
3 Substitute Q = 0.25 A × 120 s
4 Answer Q = 30 C
Quick check A current of 3.0 A flows for 50 s. Calculate the charge that flows. Then: what current moves 60 C in 30 s?
Notes: QUICK CHECK ANSWER: Q = 3.0 × 50 = 150 C. I = Q/t = 60/30 = 2.0 A. 10.1 atom structure (position, mass and charge of protons, neutrons and electrons) is included here because it explains why metals conduct.

## Slide 8
Exam practice: recap 1
Specification 10.1–10.3, 10.8–10.10 • circuits, charge and current
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Recap 1 | 8
EXAM-STYLE QUESTION
Describe two differences between a series circuit and a parallel circuit.
[2 marks]
EXAM-STYLE QUESTION
Explain what is meant by an electric current, and state what carries the current in a metal wire.
[2 marks]
EXAM-STYLE QUESTION
A current of 0.40 A flows through a motor for 3.0 minutes. Calculate the charge that flows. Give the unit.
[3 marks]
Notes: MARK SCHEME — Recap 1 (total 7 marks) Q1 [2]: Series: one loop / parallel: more than one branch or path (1); series: same current everywhere / one break stops all components; parallel: each branch works independently / same p.d. across each branch (1). Q2 [2]: Current is the rate of flow of charge (1); carried by (free/delocalised) electrons (1). Q3 [3]: t = 180 s (1); Q = I × t = 0.40 × 180 (1); = 72 C (1, unit needed).

## Slide 9
Measuring current and potential difference
Specification 10.4, 10.7, 10.16 • ammeters in series, voltmeters in parallel
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.4 | 9
Illustrative diagram — the voltmeter connects across the lamp at the two junction dots
battery
switch
A
ammeter in series
lamp
V
voltmeter in parallel (across the lamp)
I
Connecting the meters
Ammeter measures current in amps (A). Connect it in series – the current must flow through it.
Voltmeter measures potential difference (p.d.) in volts (V). Connect it in parallel, across the component.
An ammeter has very low resistance; a voltmeter has very high resistance, so neither changes the circuit much.
In a series circuit used for testing, the current is the same everywhere, so the ammeter can go anywhere in the loop.
Common mistakes
Spot what is wrong.
1 Voltmeter in series almost no current flows → the lamp does not light
2 Ammeter in parallel it short-circuits the component → very large current
3 Check trace the loop: does all the current pass through the ammeter?
4 Answer A in the loop, V across the component
Quick check A student wants to measure the p.d. across a resistor and the current through it. Describe where each meter goes.
Notes: QUICK CHECK ANSWER: ammeter in series with the resistor (in the same loop); voltmeter in parallel, connected across the two ends of the resistor. 10.16: series circuits for testing and measuring – a single loop so the ammeter reading is the current in the component under test.

## Slide 10
Potential difference: E = Q × V
Specification 10.5, 10.6 • the volt is a joule per coulomb
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.5 | 10
Illustrative diagram — energy per coulomb: gained in the battery, transferred in the lamps
12 V battery
6 V
6 V
each coulomb GAINS 12 J
in the battery
each coulomb TRANSFERS 6 J in each lamp
6 J + 6 J = 12 J
Energy per unit charge
Potential difference = the energy transferred per unit charge passed. So 1 volt = 1 joule per coulomb.
E = Q × V energy transferred (J) = charge moved (C) × potential difference (V)
RECALL: you must learn this equation.
A 12 V battery gives 12 J to every coulomb; the components transfer it all.
Worked example
A 12 V battery moves 40 C of charge round a circuit. Calculate the energy transferred.
1 Equation E = Q × V
2 Substitute E = 40 C × 12 V
3 Units C × V = C × J/C = J
4 Answer E = 480 J
Quick check A 1.5 V cell transfers 90 J of energy. Calculate the charge that flowed.
Notes: QUICK CHECK ANSWER: Q = E ÷ V = 90 ÷ 1.5 = 60 C. The diagram previews the series rule: the supply p.d. is shared (6 V + 6 V = 12 V for identical lamps).

## Slide 11
Resistance: V = I × R
Specification 10.12, 10.13 • changing the resistance changes the current
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.13 | 11
Illustrative diagram — a variable resistor controls the current through the lamp
cell
variable resistor
A
lamp
R / Ω (total) | I / A at 6.0 V
10 | 0.60
20 | 0.30
30 | 0.20
Resistance opposes the current
Resistance (ohms, Ω) is how much a component opposes the current.
Greater resistance → smaller current for the same p.d. A variable resistor lets you change the resistance, so you can control the current (e.g. dimming a lamp).
V = I × R potential difference (V) = current (A) × resistance (Ω)
RECALL: you must learn this equation. Rearrange: I = V ÷ R, R = V ÷ I.
Worked example
A current of 0.20 A flows through a 30 Ω resistor. Calculate the p.d. across it.
1 Equation V = I × R
2 Substitute V = 0.20 A × 30 Ω
3 Check bigger R or bigger I → bigger V
4 Answer V = 6.0 V
Quick check A lamp has a p.d. of 12 V across it and a current of 0.50 A through it. Calculate its resistance.
Notes: QUICK CHECK ANSWER: R = V ÷ I = 12 ÷ 0.50 = 24 Ω. Table checked in node: 6.0/10 = 0.60 A, 6.0/20 = 0.30 A, 6.0/30 = 0.20 A.

## Slide 12
Exam practice: recap 2
Specification 10.4–10.7, 10.12–10.13 • meters, p.d. and resistance
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Recap 2 | 12
EXAM-STYLE QUESTION
State how an ammeter and a voltmeter must be connected to measure the current through, and the p.d. across, a lamp.
[2 marks]
EXAM-STYLE QUESTION
A 9.0 V battery transfers 540 J of energy. Calculate the charge that flows. Use E = Q × V.
[3 marks]
EXAM-STYLE QUESTION
The p.d. across a lamp is 6.0 V and the current is 0.25 A. Calculate the resistance of the lamp. Give the unit.
[3 marks]
Notes: MARK SCHEME — Recap 2 (total 8 marks) Q1 [2]: Ammeter in series with the lamp (1); voltmeter in parallel / across the lamp (1). Q2 [3]: Q = E/V (1); = 540/9.0 (1); = 60 C (1). Q3 [3]: R = V/I (1); = 6.0/0.25 (1); = 24 Ω (1, unit needed).

## Slide 13
Series circuits: current, p.d. and resistance
Specification 10.15 • calculate currents, potential differences and resistances
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.15 | 13
Illustrative diagram — readings for a 6.0 V battery with 10 Ω and 20 Ω resistors in series
6.0 V
A
0.20 A
10 Ω
20 Ω
V
2.0 V
V
4.0 V
Total R = 10 Ω + 20 Ω = 30 Ω 2.0 V + 4.0 V = 6.0 V
Rules for series circuits
The current is the same at every point (charge is not used up).
The supply p.d. is shared between the components: V = V₁ + V₂.
Total resistance adds up: R = R₁ + R₂.
The bigger resistor gets the bigger share of the p.d. (V = I × R with the same I).
Worked example
Find the current and the p.d. across each resistor in the circuit shown.
1 Total R R = 10 + 20 = 30 Ω
2 Current I = V ÷ R = 6.0 ÷ 30 = 0.20 A
3 p.d.s V₁ = 0.20 × 10 = 2.0 V; V₂ = 0.20 × 20 = 4.0 V
4 Answer 0.20 A everywhere; 2.0 V + 4.0 V = 6.0 V ✓
Quick check A 9.0 V battery is in series with a 15 Ω and a 30 Ω resistor. Calculate the current and the p.d. across the 30 Ω resistor.
Notes: QUICK CHECK ANSWER: R = 45 Ω; I = 9.0/45 = 0.20 A; V = 0.20 × 30 = 6.0 V.

## Slide 14
Parallel circuits: currents add at junctions
Specification 10.11, 10.3 • current is conserved at a junction
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.11 | 14
Illustrative diagram — a 6.0 V battery with 10 Ω and 20 Ω resistors on separate branches
6.0 V
A
0.90 A
A
0.60 A
10 Ω
A
0.30 A
20 Ω
junction: 0.90 A in = 0.60 A + 0.30 A out
Rules for parallel circuits
Current is conserved at a junction: total current in = total current out. The branch currents add up to the supply current.
Each branch has the same p.d. as the supply (6.0 V across each resistor here).
The branch with the smaller resistance takes the bigger current (I = V ÷ R).
Worked example
Calculate each branch current and the supply current.
1 Branch 1 I₁ = 6.0 ÷ 10 = 0.60 A
2 Branch 2 I₂ = 6.0 ÷ 20 = 0.30 A
3 Junction I = I₁ + I₂
4 Answer I = 0.90 A from the battery
Quick check Two branches carry 0.40 A and 0.25 A. What does an ammeter next to the battery read? What is the p.d. across each branch if the supply is 3.0 V?
Notes: QUICK CHECK ANSWER: 0.40 + 0.25 = 0.65 A; 3.0 V across each branch. 10.11: recall that current is conserved at a junction.

## Slide 15
Why series adds resistance and parallel reduces it
Specification 10.14 • net resistance of two resistors
GRADE 7–9 STRETCH
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.14 | 15
Illustrative diagram — the same two resistors give a very different total resistance
Series: R = 30 Ω
6.0 V
10 Ω
20 Ω
I = 6.0 ÷ 30 = 0.20 A
Parallel: R ≈ 6.7 Ω
6.0 V
10 Ω
20 Ω
I = 0.60 + 0.30 = 0.90 A
Explaining the rules
Series: the charge must pass through both resistors, one after the other. More to get through → less current for the same p.d. → total resistance increases.
Parallel: adding a branch gives the charge an extra path. More charge can flow each second → more current from the supply for the same p.d. → total resistance decreases.
The total resistance in parallel is less than the smallest branch resistance.
Stretch: total resistance in parallel
Use the supply current to find the total resistance of the parallel circuit.
1 Equation R = V ÷ I
2 Substitute R = 6.0 V ÷ 0.90 A
3 Check less than 10 Ω, the smaller resistor ✓
4 Answer R = 6.7 Ω
Quick check A third resistor is added in parallel. Explain what happens to the total resistance and to the current from the supply.
Notes: QUICK CHECK ANSWER: Total resistance decreases (another path for charge) so the current from the supply increases (each branch still has the full p.d.). Stretch value checked: 6.0/0.90 = 6.667 Ω = 1/(1/10 + 1/20). Edexcel 10.14 asks for an explanation only; 1/R = 1/R₁ + 1/R₂ is not required at GCSE.

## Slide 16
Exam practice: recap 3
Specification 10.11, 10.14, 10.15 • series and parallel rules
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Recap 3 | 16
EXAM-STYLE QUESTION
A 12 V battery is connected in series with a 40 Ω and a 20 Ω resistor. Calculate the current in the circuit and the p.d. across the 40 Ω resistor.
[4 marks]
EXAM-STYLE QUESTION
In a parallel circuit, the branch currents are 0.35 A and 0.15 A. State the current from the supply.
[1 mark]
EXAM-STYLE QUESTION
Explain why adding a resistor in parallel with another resistor decreases the total resistance of a circuit.
[3 marks]
Notes: MARK SCHEME — Recap 3 (total 8 marks) Q1 [4]: R = 60 Ω (1); I = 12/60 = 0.20 A (1); V = I × R = 0.20 × 40 (1); = 8.0 V (1). Q2 [1]: 0.50 A (1). Q3 [3]: Provides an extra path / branch for the charge (1); so more charge flows per second / total current increases (1); for the same p.d., so R = V/I is smaller (1).

## Slide 17
Core Practical: circuit and method
Specification 10.17 • investigate V, I and R for a resistor and a filament lamp
CORE PRACTICAL
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
CP 10.17 | 17
Illustrative diagram — test component (resistor, then filament lamp) with ammeter and voltmeter
battery
switch
variable
resistor
test component
A
ammeter
V
voltmeter
then swap in a lamp:
filament
lamp
Method (part a)
Set up the circuit. Close the switch only while taking readings.
Adjust the variable resistor to change the current. Record the p.d. (voltmeter) and current (ammeter).
Take readings for about 6–8 different settings, from 0 V upwards.
Reverse the battery connections and repeat to get negative values.
Calculate R = V ÷ I for each pair. Repeat with a filament lamp.
Plot current (y-axis) against p.d. (x-axis).
Tips for accurate results
1 Switch off between readings so the resistor does not warm up
2 Zero check meters read 0 with the switch open
3 Range use a wide range of p.d. values, evenly spaced
4 Answer repeat each reading and calculate a mean
Quick check What is the variable resistor for in this circuit? Why is the voltmeter not in the main loop?
Notes: QUICK CHECK ANSWER: The variable resistor changes the current (and so the p.d. across the test component) so a range of readings can be taken. The voltmeter must be in parallel across the component to measure the p.d. across it; in series it would stop the current (very high resistance). Apparatus: battery or low-voltage d.c. supply, switch, variable resistor (rheostat), ammeter, voltmeter, resistor, 6 V filament lamp, connecting leads.

## Slide 18
Core Practical: variables and testing circuits
Specification 10.17 • part (b): test series and parallel circuits using resistors and filament lamps
CORE PRACTICAL
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
CP 10.17 | 18
Illustrative diagram — what you change, measure and keep the same in part (a)
Independent variable (you change)
potential difference across the component (V), using the variable resistor
Dependent variable (you measure)
current through the component (A)
Control variables (keep the same)
the same component • its temperature (switch off between readings) • the same meters
Part (b): testing series and parallel
Build two lamps (or resistors) in series. Measure the current at different points and the p.d. across each one and across the supply.
Rebuild them in parallel. Measure the current in each branch and from the supply, and the p.d. across each branch.
Compare with the rules: series – same current, p.d.s add; parallel – currents add, same p.d.
Safety
Hazard → risk → control
1 Hot lamp filament lamps and resistors get hot → burns; do not touch, switch off between readings
2 Short circuit wires get very hot → check the circuit before switching on
3 Supply use a low-voltage supply only (never mains)
4 Answer switch off before changing any connection
Quick check Name the independent and dependent variables in part (a). Why is the temperature of the resistor a control variable?
Notes: QUICK CHECK ANSWER: IV = p.d. across the component; DV = current through it. Temperature is controlled because the resistance of a metal increases as it gets hotter, which would change the results for a fixed resistor.

## Slide 19
Core Practical: results and graph
Specification 10.17 • sample results for a resistor and a filament lamp
CORE PRACTICAL
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
CP 10.17 | 19
Illustrative diagram — sample data plotted to scale; current on the y-axis
0
1
2
3
4
5
6
0.00
0.05
0.10
0.15
0.20
0.25
0.30
0.35
potential difference / V
current / A
resistor
filament lamp
p.d. / V | I resistor / A | I lamp / A | R lamp / Ω
0.0 | 0.00 | 0.00 | –
1.0 | 0.05 | 0.13 | 7.7
2.0 | 0.10 | 0.20 | 10
3.0 | 0.15 | 0.24 | 13
4.0 | 0.20 | 0.27 | 15
5.0 | 0.25 | 0.29 | 17
6.0 | 0.30 | 0.30 | 20
What the results show
Resistor: straight line through the origin, so I ∝ V and R is constant: 6.0 ÷ 0.30 = 20 Ω.
Lamp: the curve gets less steep; R rises from about 7.7 Ω to 20 Ω as the filament heats up.
R lamp = V ÷ I, rounded to 2 significant figures.
Quick check Use the table to calculate the resistance of the lamp at 2.0 V and at 6.0 V. What happens to its resistance?
Notes: QUICK CHECK ANSWER: 2.0/0.20 = 10 Ω; 6.0/0.30 = 20 Ω. The resistance increases as the p.d. (and so the temperature of the filament) increases. Sample data from models checked in node: resistor I = V/20; lamp I = V/(5 + 2.5V), rounded to 2 d.p.

## Slide 20
Core Practical: errors and improvements
Specification 10.17 • evaluating the method
CORE PRACTICAL
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
CP 10.17 | 20
Illustrative diagram — two common sources of error in the circuits practical
0.02
A (switch open)
Zero error: the meter reads 0.02 A with no current. Subtract 0.02 A from every reading, or reset the zero.
Heating: current warms the resistor, so its resistance rises during the experiment. Switch off between readings; use small currents.
Digital meters: no parallax error, but the last digit may flicker → record the mean value.
Sources of error
Zero error on a meter → a systematic error in every reading; check with the switch open.
Temperature rise of the resistor or wires → resistance changes; switch off between readings.
Resolution of the meters: an ammeter reading to 0.01 A gives poor precision for small currents.
Poor connections add extra resistance → check that all leads are tight.
Improving the investigation
1 Repeat take each reading 3 times and calculate a mean
2 More points take more readings where the lamp graph curves most
3 Precision use meters with a higher resolution (e.g. mA range)
4 Answer more reliable values of R and a better curve of best fit
Quick check A student leaves the current switched on for the whole experiment with the fixed resistor. How might the graph change?
Notes: QUICK CHECK ANSWER: The resistor warms up so its resistance increases; at higher p.d.s the current would be lower than expected, so the line would curve slightly towards the p.d. axis instead of being straight.

## Slide 21
Exam practice: recap 4
Specification 10.17 • Core Practical: electrical circuits
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Recap 4 | 21
EXAM-STYLE QUESTION
A student investigates how the current through a filament lamp depends on the p.d. across it. Describe where the ammeter and voltmeter are connected, and state the purpose of the variable resistor.
[3 marks]
EXAM-STYLE QUESTION
At 4.0 V the current through the lamp is 0.25 A. Calculate the resistance of the lamp.
[2 marks]
EXAM-STYLE QUESTION
Explain why the student should switch off the circuit between readings when investigating a fixed resistor.
[2 marks]
Notes: MARK SCHEME — Recap 4 (total 7 marks) Q1 [3]: Ammeter in series with the lamp (1); voltmeter in parallel across the lamp (1); variable resistor changes the current / p.d. so a range of readings can be taken (1). Q2 [2]: R = V/I = 4.0/0.25 (1); = 16 Ω (1). Q3 [2]: Current heats the resistor / it gets hot (1); its resistance would change / increase, so it would not be a fair test (temperature is a control variable) (1).

## Slide 22
I–V graphs: fixed resistor and filament lamp
Specification 10.18 • how current varies with p.d., and what this means for resistance
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.18 | 22
Illustrative diagram — drawn to scale: 20 Ω resistor and a 6 V, 0.3 A filament lamp
-6
-4
-2
2
4
6
-0.3
-0.2
-0.1
-0.0
0.1
0.2
0.3
0.4
0
p.d. / V
current / A
fixed resistor
filament lamp
reversed p.d. → same shape, upside down
Reading the I–V graphs
Fixed resistor (constant temperature): a straight line through the origin. Current ∝ p.d., so R is constant.
Filament lamp: an S-shaped curve through the origin. It gets less steep as the p.d. increases.
Why: a bigger current makes the filament hotter. The metal ions vibrate more, electrons collide with them more often, so resistance increases.
Find R at any point using R = V ÷ I (not the gradient).
Worked example
Use the graph: the lamp has I = 0.20 A at 2.0 V and I = 0.30 A at 6.0 V.
1 At 2.0 V R = 2.0 ÷ 0.20 = 10 Ω
2 At 6.0 V R = 6.0 ÷ 0.30 = 20 Ω
3 Compare resistor: 6.0 ÷ 0.30 = 20 Ω at every point
4 Answer lamp resistance doubles as it heats up
Quick check Sketch the I–V graph of a filament lamp. Explain why it is not a straight line.
Notes: QUICK CHECK ANSWER: S-shaped curve through the origin, flattening at high positive and negative p.d. As the current increases the filament gets hotter; ions vibrate more, electrons collide more, so resistance increases and the current rises less for each extra volt. Models plotted: resistor I = V/20; lamp I = V/(5 + 2.5|V|).

## Slide 23
I–V graph: the diode
Specification 10.18 • current flows in one direction only
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.18 | 23
Illustrative diagram — drawn to scale for a silicon diode: it conducts above about 0.6 V forward
-1.0
-0.8
-0.6
-0.4
-0.2
0.2
0.4
0.6
0.8
1.0
-10
10
20
30
40
0
p.d. / V
current / mA
≈ 0.6 V
reverse: almost no current
(very high resistance)
forward: low
resistance
forward →
A one-way valve for current
In the reverse direction the diode has a very high resistance: almost no current flows.
In the forward direction there is very little current until about 0.6 V; then the current rises steeply – the resistance becomes low.
Uses: protecting circuits from a battery connected the wrong way; changing a.c. into d.c.
An LED is a diode that gives out light when a forward current flows.
Compare the three graphs
Which component…
1 Constant R fixed resistor: straight line through origin
2 R rises with I filament lamp: S-curve that flattens
3 One direction diode: zero in reverse, steep after ≈ 0.6 V
4 Answer R = V ÷ I at each point tells you the resistance
Quick check Describe what happens to the current through a diode when the p.d. across it is reversed. What does this tell you about its resistance?
Notes: QUICK CHECK ANSWER: Almost no current flows in the reverse direction, so the diode has a very high resistance in reverse (and a low resistance forward, above about 0.6 V). Model: I = A(e^(V/0.045) − 1) mA, scaled so I(0.75 V) = 30 mA; I(0.6 V) = 1.07 mA, I(0.7 V) = 9.9 mA.

## Slide 24
Sensors: LDRs and thermistors
Specification 10.19, 10.20 • resistance that depends on light or temperature
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.19 | 24
Illustrative diagram — typical curves, drawn to scale for one LDR and one NTC thermistor
0
250
500
750
1000
0
5
10
15
20
25
light intensity / lux
resistance / kΩ
0
25
50
75
100
0
10
20
30
temperature / °C
resistance / kΩ
LDR
Thermistor (NTC)
Two sensing components
LDR (light-dependent resistor): resistance decreases as light intensity increases. High resistance in the dark.
Uses: street lights and security lights that switch on when it gets dark.
Thermistor (NTC): resistance decreases as temperature increases.
Uses: thermostats, fire alarms, car engine and oven temperature sensors.
Read the graphs
What happens to the current through each sensor connected to a fixed p.d.?
1 LDR in bright light R falls → current increases
2 Thermistor heated R falls → current increases
3 Dark / cold R high → current small
4 Answer the current can be used to switch a lamp, heater or alarm
Quick check A thermistor is moved from a fridge (5 °C) into a warm room (25 °C). Describe what happens to its resistance and to the current through it.
Notes: QUICK CHECK ANSWER: Its resistance decreases (NTC) so the current through it increases (for the same p.d.). From the graph: about 22 kΩ at 5 °C to 10 kΩ at 25 °C. Models: LDR R = 100 L^-0.7 kΩ; thermistor R = 10 e^(-(T-25)/25) kΩ.

## Slide 25
Using circuits to explore resistance
Specification 10.21 • filament lamps, diodes, thermistors and LDRs
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.21 | 25
Illustrative diagram — thermistor in a water bath: measure V and I at each temperature
battery
A
ammeter
V
voltmeter
thermistor
thermometer
water: heat with a kettle or add ice
Designing the circuit
Use a series circuit with an ammeter, and a voltmeter across the device. Calculate R = V ÷ I for each condition.
Thermistor: put it in water at different temperatures (measured with a thermometer).
LDR: change the light intensity, e.g. move a lamp to different distances, in a darkened room.
Filament lamp and diode: use a variable resistor to change the p.d.; reverse the supply to test the other direction.
Worked example
At 20 °C the voltmeter reads 6.0 V and the ammeter reads 0.50 mA.
1 Convert I = 0.50 mA = 0.00050 A
2 Equation R = V ÷ I
3 Substitute R = 6.0 ÷ 0.00050
4 Answer R = 12 000 Ω (12 kΩ)
Quick check Describe how you would change the light intensity on an LDR fairly. Name one control variable.
Notes: QUICK CHECK ANSWER: Move a lamp to measured distances from the LDR (or use a light meter) in a darkened room. Control: the same lamp / same p.d. of supply / same LDR / no other light sources. Worked check: 6.0/0.00050 = 12000 Ω.

## Slide 26
Exam practice: recap 5
Specification 10.18–10.21 • I–V graphs and sensors
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Recap 5 | 26
EXAM-STYLE QUESTION
Describe the shape of the I–V graph for a filament lamp and explain why it has this shape.
[3 marks]
EXAM-STYLE QUESTION
Describe how the current through a diode depends on the direction of the p.d. across it.
[2 marks]
EXAM-STYLE QUESTION
Describe how the resistance of a thermistor changes with temperature, and give one use of a thermistor.
[2 marks]
Notes: MARK SCHEME — Recap 5 (total 7 marks) Q1 [3]: Curve through the origin that gets less steep / S-shape (1); as current increases the filament gets hotter (1); so its resistance increases (ions vibrate more, more collisions) (1). Q2 [2]: Current flows in one (forward) direction only / once p.d. above about 0.6 V (1); (almost) no current in the reverse direction – very high resistance (1). Q3 [2]: Resistance decreases as temperature increases (1); any one: thermostat / fire alarm / temperature sensor (1).

## Slide 27
The heating effect of an electric current
Specification 10.22, 10.23, 10.24 • collisions between electrons and ions
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.22 | 27
Illustrative diagram — model of a metal: positive ions in a lattice, free electrons moving through
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
free electron (−)
ion vibrates more → metal heats up
Why a current heats a wire
When there is a current in a resistor, energy is transferred that heats the resistor.
The current does work against the resistance. Energy is dissipated as thermal energy to the surroundings.
Model: moving electrons collide with the ions in the lattice. They transfer energy to the ions, which vibrate more → the temperature rises.
Hotter ions vibrate more, so collisions happen more often → resistance increases (filament lamp).
Explain it in steps
Explain why a resistor gets hot when there is a current in it.
1 Electrons the current is a flow of electrons through the metal
2 Collisions electrons collide with the lattice ions
3 Energy energy is transferred to the ions, which vibrate more
4 Answer the thermal energy store of the resistor increases → it heats up
Quick check Use the lattice model to explain why the resistance of a metal wire increases when it gets hot.
Notes: QUICK CHECK ANSWER: When the wire is hotter the ions vibrate more (with greater amplitude) (1), so the electrons collide with them more often / their flow is impeded more (1), so the resistance increases. 10.22 recall; 10.23 energy dissipated as thermal energy in the surroundings; 10.24 collisions between electrons and ions in the lattice.

## Slide 28
The heating effect: useful or a problem?
Specification 10.25, 10.26 • reducing unwanted energy transfer
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.26 | 28
Illustrative diagram — low-resistance wires waste less energy as heat
thin, long, high R
thick, short copper, low R
more heating, more energy wasted
less heating, less energy wasted
Advantages (useful)
kettles, toasters and electric heaters
hair dryers and irons
the filament of a lamp glows
a fuse melts to break a circuit
Disadvantages
energy wasted in wires and devices
lower efficiency
components can overheat and fail
risk of fire; cooling fans or vents may be needed
Reducing unwanted heating
Unwanted heating in connecting wires wastes energy. Use low-resistance wires: thick, short, made of a good conductor such as copper.
Lower resistance → less energy dissipated per second for the same current (P = I² × R).
Other ways: lubricate moving parts in motors; use LEDs instead of filament lamps.
Think it through
Why do the cables for an electric cooker have thicker copper wires than a lamp cable?
1 Current a cooker draws a much larger current
2 Heating a large current in a wire causes a lot of heating
3 Fix a thicker wire has a lower resistance
4 Answer less heating → cable does not overheat; less energy wasted
Quick check Give one advantage and one disadvantage of the heating effect of an electric current.
Notes: QUICK CHECK ANSWER: Advantage – e.g. used in kettles/heaters/toasters, fuses. Disadvantage – e.g. energy wasted in wires/devices (reduces efficiency), overheating/fire risk. 10.25: ways of reducing unwanted energy transfer through low-resistance wires.

## Slide 29
Energy and power: E = I × V × t and P = E ÷ t
Specification 10.27, 10.28, 10.29 • power is energy transferred per second
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.27 | 29
Illustrative diagram — energy transferred by an electric kettle each second
mains supply
230 V
kettle element
I = 9.0 A
electrical
work
thermal energy store
of the water (useful)
thermal store of the
surroundings (wasted)
Each second: E = 9.0 A × 230 V × 1 s = 2070 J
so the power is
P = 2070 W (about 2.1 kW)
Energy and power equations
E = I × V × t energy transferred (J) = current (A) × p.d. (V) × time (s)
GIVEN on the Physics Equations List – select and use it.
Power is the energy transferred per second, measured in watts (W). 1 W = 1 J/s.
P = E ÷ t power (W) = energy transferred (J) ÷ time taken (s)
RECALL: you must learn this equation.
Worked example
The kettle (9.0 A, 230 V) is switched on for 2.0 minutes. Calculate the energy transferred.
1 Equation E = I × V × t
2 Convert t = 2.0 × 60 = 120 s
3 Substitute E = 9.0 × 230 × 120
4 Answer E = 248 400 J ≈ 2.5 × 10⁵ J
Quick check A lamp transfers 1800 J of energy in 60 s. Calculate its power. Give the unit.
Notes: QUICK CHECK ANSWER: P = E ÷ t = 1800 ÷ 60 = 30 W. Worked: 9.0 × 230 × 120 = 248400 J. Each second: 9.0 × 230 = 2070 J → 2070 W.

## Slide 30
Electrical power: P = I × V and P = I² × R
Specification 10.30, 10.31, 10.32 • power depends on current and p.d.
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.31 | 30
Illustrative diagram — measuring the power of a heater: P = ammeter reading × voltmeter reading
12 V supply
A
3.0 A
heater 4.0 Ω
V
12 V
Where P = I²R comes from: P = I × V and V = I × R, so P = I × (I × R) = I² × R
Power in a circuit device
The power of a device = the rate at which energy is transferred from the supply to it. It depends on the current and the p.d. across it.
P = I × V electrical power (W) = current (A) × potential difference (V)
P = I² × R electrical power (W) = current² (A²) × resistance (Ω)
RECALL: learn both equations.
A hairdryer on 230 V taking 5.0 A: P = 5.0 × 230 = 1150 W.
Worked example
A current of 3.0 A flows through a 4.0 Ω heater. Calculate its power.
1 Equation P = I² × R
2 Substitute P = 3.0² × 4.0 = 9.0 × 4.0
3 Check V = 3.0 × 4.0 = 12 V; P = 3.0 × 12 = 36 W ✓
4 Answer P = 36 W
Quick check A current of 0.50 A flows through a 12 Ω resistor. Calculate the power. Square the current first!
Notes: QUICK CHECK ANSWER: P = 0.50² × 12 = 0.25 × 12 = 3.0 W. Common error: 0.50 × 12 = 6 W (forgot to square). Hairdryer: 1150 W. Stretch idea: a 10 A current in a cable of resistance 0.20 Ω wastes 10² × 0.20 = 20 W.

## Slide 31
Exam practice: recap 6
Specification 10.22–10.32 • heating, energy and power
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Recap 6 | 31
EXAM-STYLE QUESTION
Explain why a wire gets hot when there is a current in it.
[2 marks]
EXAM-STYLE QUESTION
A hairdryer takes a current of 4.0 A from the 230 V mains. Calculate its power.
[2 marks]
EXAM-STYLE QUESTION
A current of 2.0 A passes through a 15 Ω resistor for 5.0 minutes. Calculate the power and the energy transferred.
[3 marks]
Notes: MARK SCHEME — Recap 6 (total 7 marks) Q1 [2]: Electrons collide with ions in the (metal) lattice (1); energy transferred to the ions / they vibrate more, so the thermal energy store / temperature increases (1). Q2 [2]: P = I × V = 4.0 × 230 (1); = 920 W (1). Q3 [3]: P = I²R = 2.0² × 15 = 60 W (1); t = 300 s (1); E = P × t = 60 × 300 = 18 000 J (1). Allow E = I × V × t with V = 30 V.

## Slide 32
Direct and alternating current
Specification 10.34–10.37 • d.c. from cells, a.c. from the mains
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.34 | 32
Illustrative diagram — to scale: a 12 V battery (top) and the UK mains, 50 Hz (bottom)
0
10
20
30
40
0
5
10
15
time / ms
p.d. / V
d.c.: 12 V, constant
0
10
20
30
40
-400
-200
200
400
one cycle = 20 ms
p.d. / V
time
/ ms
a.c.: direction keeps changing
Two kinds of supply
Direct current (d.c.): charge moves in one direction only. Cells and batteries supply d.c.
Alternating current (a.c.): the movement of charge changes direction many times a second, because the p.d. alternates between positive and negative.
UK mains: a.c., frequency 50 Hz, p.d. about 230 V.
Mains a.c. is used to transfer energy to motors and heaters in the home; batteries supply portable devices.
Worked example
The UK mains has a frequency of 50 Hz. How long does one cycle take?
1 Meaning 50 Hz = 50 cycles every second
2 Equation time for one cycle T = 1 ÷ f
3 Substitute T = 1 ÷ 50 Hz
4 Answer T = 0.020 s (20 ms)
Quick check State two differences between the supply from a battery and the UK mains supply.
Notes: QUICK CHECK ANSWER: battery d.c. (one direction) vs mains a.c. (changes direction); battery small p.d. (e.g. 1.5–12 V) vs mains about 230 V; mains 50 Hz. The a.c. trace peaks at about 325 V: 230 V is the effective (r.m.s.) value – not needed at GCSE. 10.33 (energy from batteries and a.c. mains to motors and heating devices) is covered here and on the power-ratings slide.

## Slide 33
Mains wiring: live, neutral and earth
Specification 10.38, 10.39, 10.43 • the three wires in a UK plug
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.38 | 33
Illustrative diagram — inside a UK three-pin plug (back removed)
earth (green/yellow)
0 V
fuse (in the live wire)
live (brown)
about 230 V
neutral (blue)
close to 0 V
cable grip
The three wires
Live (brown): carries the alternating p.d. from the supply. The p.d. between live and earth is about 230 V.
Neutral (blue): completes the circuit; it is at (or close to) 0 V. So there is a large p.d. between live and neutral.
Earth (green/yellow): a safety wire at 0 V, connected to metal cases. It carries a current only if there is a fault.
A live wire can be dangerous even when the switch is off (e.g. a switch wrongly fitted in the neutral). Touching it connects the live wire to earth through your body → a large current → electric shock.
Explain it in steps
Why can touching a live wire kill you, even if the appliance is switched off?
1 p.d. the live wire is at about 230 V; you and the ground are at 0 V
2 Path your body connects the live wire to earth
3 Current a large current flows through you to earth
4 Answer electric shock – possibly fatal
Quick check State the colour of the live, neutral and earth wires and the p.d. of each relative to earth.
Notes: QUICK CHECK ANSWER: live – brown – about 230 V; neutral – blue – about 0 V; earth – green and yellow stripes – 0 V. 10.38 difference in potential between live and neutral; 10.39 danger of any connection between live and earth; 10.43 p.d. between live and earth about 230 V.

## Slide 34
Fuses, circuit breakers and the earth wire
Specification 10.41, 10.42 • how a fault is made safe
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.41 | 34
Illustrative diagram — a fault: the live wire touches the metal case of a heater
mains
L
N
E
metal case
fuse
switch
heating
element
neutral
earth
FAULT: live touches case
large current flows to earth → fuse melts → live disconnected
Making a fault safe
Earth wire: connects the metal case to earth. If the live wire touches the case, a large current flows to earth through this low-resistance path.
Fuse: a thin wire that melts when the current is too large, breaking the circuit. Circuit breaker: a switch that trips automatically – it acts faster and can be reset.
Switches and fuses go in the live wire, so that when they open, the appliance is disconnected from the high p.d.
Worked example: choosing a fuse
A 2.3 kW kettle runs on 230 V. Fuses: 3 A, 5 A, 13 A. Which fuse?
1 Equation P = I × V, so I = P ÷ V
2 Substitute I = 2300 W ÷ 230 V
3 Current I = 10 A
4 Answer choose the 13 A fuse (just above 10 A)
Quick check Explain why a fuse must be in the live wire and not the neutral wire.
Notes: QUICK CHECK ANSWER: If the fuse melted in the neutral wire, the appliance would still be connected to the live wire at 230 V, so touching it could still give a shock. In the live wire, a melted fuse disconnects the appliance from the high p.d. Fuse calc: 2300/230 = 10 A → 13 A. (A 60 W lamp: 60/230 ≈ 0.26 A → 3 A fuse.) Edexcel 10.41 says "fuses or circuit breakers"; no tier marker found.

## Slide 35
Power ratings of domestic appliances
Specification 10.33, 10.40 • energy transferred from the mains or batteries to useful stores
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
10.40 | 35
Illustrative diagram — bar lengths drawn to scale (typical power ratings)
appliance
power / W
energy goes mainly to…
kettle
2300
thermal store of water
hairdryer
1200
thermal + kinetic (motor)
microwave
800
thermal store of food
vacuum cleaner
600
kinetic store of the motor
television
100
light and sound (radiation)
LED lamp
10
light (radiation)
phone charger
5
chemical store of battery
What a power rating tells you
The power rating is the energy transferred per second when the appliance is used: a 2300 W kettle transfers 2300 J every second.
Higher power → more energy transferred from the supply to the appliance’s useful stores (and wasted to the surroundings) in the same time.
Energy transferred = power × time (E = P × t). Mains devices use a.c.; portable devices are powered by batteries (d.c.).
Efficiency = useful energy transferred ÷ total energy supplied.
Worked example
A 2000 W heater is used for 30 minutes. A 2000 W kettle transfers 1800 J usefully each second.
1 Energy E = P × t = 2000 × (30 × 60)
2 Result E = 3.6 × 10⁶ J
3 Efficiency kettle = 1800 ÷ 2000
4 Answer efficiency = 0.9 (90%)
Quick check Calculate the energy transferred by a 10 W LED lamp left on for 1 hour.
Notes: QUICK CHECK ANSWER: E = P × t = 10 × 3600 = 36 000 J. 10.33: in different domestic devices energy is transferred from batteries and the a.c. mains to the energy of motors and heating devices. 10.40: power ratings and the changes in stored energy. Efficiency links back to Topic 3.

## Slide 36
Exam practice: recap 7
Specification 10.33–10.43 • a.c., d.c. and mains safety
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Recap 7 | 36
EXAM-STYLE QUESTION
Describe the difference between direct current and alternating current.
[2 marks]
EXAM-STYLE QUESTION
State the frequency and the potential difference of the UK domestic mains supply.
[2 marks]
EXAM-STYLE QUESTION
The live wire inside a metal toaster comes loose and touches the metal case. Explain how the earth wire and the fuse protect the user.
[4 marks]
Notes: MARK SCHEME — Recap 7 (total 8 marks) Q1 [2]: d.c.: charge flows in one direction only (1); a.c.: the direction of flow of charge changes / keeps reversing (1). Q2 [2]: 50 Hz (1); about 230 V (1). Q3 [4]: Earth wire connects the case to earth / provides a low-resistance path (1); a large current flows through the live and earth wires (1); the fuse melts / blows (1); this breaks the circuit / disconnects the live wire so the case is no longer live (1).

## Slide 37
Summary: equations
Topic 10 equations • RECALL = learn it; GIVEN = on the Physics Equations List
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Equations | 37
Equation | In words (units) | Recall or given? | Spec
Q = I × t | charge (C) = current (A) × time (s) | RECALL | 10.9
E = Q × V | energy transferred (J) = charge moved (C) × potential difference (V) | RECALL | 10.6
V = I × R | potential difference (V) = current (A) × resistance (Ω) | RECALL | 10.13
E = I × V × t | energy transferred (J) = current (A) × potential difference (V) × time (s) | GIVEN | 10.27
P = E ÷ t | power (W) = energy transferred (J) ÷ time taken (s) | RECALL | 10.29
P = I × V | electrical power (W) = current (A) × potential difference (V) | RECALL | 10.31
P = I² × R | electrical power (W) = current squared (A²) × resistance (Ω) | RECALL | 10.32
Quick check Cover the middle column. For each equation, say every quantity and its unit aloud.
Notes: QUICK CHECK: self-check against the table. Recall list: Q = It, E = QV, V = IR, P = E/t, P = IV, P = I²R. Given on the Physics Equations List: E = I × V × t (spec 10.27 says “use”, not “recall and use”). See SPEC_T10.md for sources.

## Slide 38
Summary: key words
Topic 10 Electricity and circuits • learn these definitions
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Key words | 38
Electric current
Rate of flow of charge, in amps (A); carried by electrons in metals.
Charge
Measured in coulombs (C): Q = I × t.
Potential difference
Energy transferred per unit charge; 1 V = 1 J/C.
Resistance
Opposition to current, in ohms (Ω): R = V ÷ I.
Series circuit
One loop: same current everywhere; p.d. is shared; resistances add.
Parallel circuit
Separate branches: same p.d. on each; branch currents add.
Ammeter / voltmeter
Ammeter in series (current); voltmeter in parallel (p.d.).
Filament lamp
Resistance increases as it gets hotter: curved I–V graph.
Diode
Lets current flow in one direction only; very high resistance in reverse.
LDR
Light-dependent resistor: resistance falls as light intensity rises.
Thermistor
NTC: resistance falls as temperature rises.
Power
Energy transferred per second, in watts (W): P = I × V.
Direct current
d.c.: charge flows in one direction only (cells, batteries).
Alternating current
a.c.: direction keeps changing; UK mains 230 V, 50 Hz.
Fuse
Thin wire in the live wire that melts if the current is too large.
Earth wire
Green/yellow safety wire connecting metal cases to earth (0 V).
Notes: Use as a cover-and-recall activity: hide the definitions, students say them, then reveal.

## Slide 39
Full exam question
Specification 10.6–10.18, 10.31–10.32 • answer every part • 13 marks
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Full question | 39
A student investigates a filament lamp using a battery, a variable resistor, an ammeter and a voltmeter. At 3.0 V the current is 0.20 A.
(a) Name the component the student adjusts to change the current in the circuit.
[1 mark]
(b) Calculate the resistance of the lamp when the p.d. is 3.0 V.
[2 marks]
(c) Calculate the charge that flows through the lamp in 2.0 minutes at 0.20 A.
[2 marks]
(d) Calculate the energy transferred to the lamp by this charge. Use your answer to (c).
[2 marks]
(e) At 6.0 V the current is 0.30 A, so the resistance is now 20 Ω. Explain why the resistance of the lamp has increased.
[3 marks]
(f) Calculate the power of the lamp at 6.0 V using P = I² × R. Show that P = I × V gives the same answer.
[3 marks]
Total: 13 marks
Notes: MARK SCHEME — full question (total 13 marks) (a) [1]: variable resistor / rheostat (1). (b) [2]: R = V/I = 3.0/0.20 (1); = 15 Ω (1). (c) [2]: Q = I × t = 0.20 × 120 (1); = 24 C (1). (d) [2]: E = Q × V = 24 × 3.0 (1); = 72 J (1). ECF from (c). (e) [3]: Larger current makes the filament hotter (1); metal ions vibrate more (1); electrons collide with ions more often, so resistance increases (1). (f) [3]: P = 0.30² × 20 (1); = 1.8 W (1); P = I × V = 0.30 × 6.0 = 1.8 W (1).

## Slide 40
Homework
Topic 10 Electricity and circuits • 17 marks • about 30 minutes
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Homework | 40

## Slide 41
Homework
Answer in full sentences • show all working • 17 marks
Pearson Edexcel GCSE (9–1) Physics (1PH0) | Topic 10 Electricity and circuits | Higher & Foundation
Homework | 41
Answer every question. Show your working for calculations.
1 Write down the equation that links potential difference, current and resistance.
[1 mark]
2 A charge of 150 C passes through a heater in 60 s. Calculate the current.
[2 marks]
3 Explain why switches and fuses are connected in the live wire of an appliance.
[2 marks]
4 A kettle takes 8.0 A from the 230 V mains. Calculate its power, and choose a fuse: 3 A, 5 A or 13 A.
[3 marks]
5 A 12 V car heater takes a current of 3.0 A for 10 minutes. Calculate the energy transferred. Use E = I × V × t.
[3 marks]
6 Describe how you would investigate how the current through a filament lamp varies with the potential difference across it. Explain how you would use your results to show how the resistance of the lamp changes.
[6 marks]
Notes: MARK SCHEME — homework (total 17 marks) 1 [1]: potential difference = current × resistance / V = I × R (1). 2 [2]: I = Q/t = 150/60 (1); = 2.5 A (1). 3 [2]: So that when the switch is off / the fuse melts, the appliance is disconnected from the live wire / high p.d. (1); so there is no danger of a shock from touching it (1). 4 [3]: P = I × V = 8.0 × 230 (1); = 1840 W (1); 13 A fuse – just above the normal current of 8.0 A (1). 5 [3]: t = 600 s (1); E = 3.0 × 12 × 600 (1); = 21 600 J / 2.16 × 10⁴ J (1). 6 [6]: Levels-based mark scheme (6 marks). Answers are marked holistically; use the indicative content below. Level 0 (0 marks): no rewardable material. Level 1 (1–2 marks): demonstrates elements of physics understanding, some of which is inaccurate; understanding of scientific ideas lacks detail; presents an explanation with some structure and coherence. Level 2 (3–4 marks): demonstrates physics understanding which is mostly relevant but may include some inaccuracies; understanding of scientific ideas is not fully detailed and/or developed; presents an explanation that has a structure which is mostly clear, coherent and logical. Level 3 (5–6 marks): demonstrates accurate and relevant physics understanding throughout; understanding of the scientific ideas is detailed and fully developed; presents an explanation that has a well-developed structure which is clear, coherent and logical. Indicative content: • Circuit: battery / power supply, switch, variable resistor, ammeter in series with the lamp, voltmeter in parallel across the lamp. • Adjust the variable resistor to change the p.d. across the lamp. • Record pairs of readings of p.d. and current (e.g. 6–8 values from 0 V to 6 V). • Reverse the supply connections to get negative values. • Repeat readings and calculate means; switch off between readings. • Plot a graph of current (y) against p.d. (x); draw a smooth curve of best fit. • Calculate R = V ÷ I at several points. • Graph is a curve that gets less steep / R increases as the p.d. increases. • Because the filament gets hotter, ions vibrate more, more collisions with electrons. • Safety: lamp gets hot – do not touch; low-voltage supply.